## Slide 1: Chapter 7
HCS12 Programming in C

## Slide 2: Objectives for Chapter 7
Examine C data types for the HCS12
Code C programs for time delay and I/O operations
Code C programs for I/O bit manipulation
Code C programs for logic and arithmetic operations
Code C programs for ASCII and BCD data conversion
Code C programs for binary (hex) to decimal conversion
Code C programs for data serialization
Understand C compiler RAM and ROM allocation

## Slide 3: Why program the HCS12 in C?
Compilers produce hex files that we download into the ROM of the microcontroller.
The resulting file size is a main concern for microcontroller programmers
  Limited on chip ROM
  Code space is limited to 512k
  Programming in assembly language takes up less space than C
However…
  Easier and less time consuming programming in C
  C is easier to modify and update
  One can use code available in function libraries
  C code is more portable to other microcontrollers

## Slide 4: C data types for the HCS12
Data Type | Size in Bits | Data Range/Usage
Unsigned char | 8 | 0 to 255
Char | 8 | -128 to +127
Unsigned int | 16 | 0 to 65,535
Int | 16 | -32,768 to +32,767
Unsigned short | 16 | 0 to 65,535
Short | 16 | -32,768 to +32,767
Unsigned short long | 24 | 0 to 16,777,215
Short long | 24 | -8,388,608 to +8,388,607
Unsigned long | 32 | 0 to 4,294,967,295
Long | 32 | -2,147,483,648 to +2,147,483,647

## Slide 5: Some comments about unsigned char
Character data type is most natural type for many applications.
Unsigned character type is one of the most used in HCS12 programming
C compilers default to character type unless keyword “unsigned” is used
Programmers should use unsigned character over other data types whenever possible
Note the following example

## Slide 6: Example C code to send values 00 – FF to PORTB
#include <mc9s12dp512.h> // for DDRB and PORTB declarations
void main(void)
{
unsigned char z;
DDRB = 0xFF; // PORTB is output
for (z=0;z<=255;z++)
PORTB = z;
while (1); // needed if running in hardware
}

## Slide 7: C program to send ASCII to PORTB
#include <mc9s12dp512.h> // Port B declarations
void main (void)
{
unsigned char mynum[ ] = “0123456789ABCD”; // ASCII string in RAM
unsigned char z; // counter
DDRB = 0xFF; // Port B is output
for (z=0; z<10; z++)
PORTB = mynum[z];
while (1); // stay here
}

## Slide 8: Program to toggle PORTB forever
#include <mc9s12dp512 // for PORTB declarations
void main(void)
{
DDRB = 0xFF // PORTB is output
for (;;) // Loop forever
{
PORTB = 0x55; // 0x declares hex data
PORTB = 0xAA;
}
}

## Slide 9: Signed Characters
8 bit data type representing signed 7 bit numbers
MSB contains sign, if 0 then positive, if 1 then negative
Values -128 to +127 may be represented
Must be used when we are dealing with any data that may take on a value in the above range
This the default character data type
Note the following example

## Slide 10: C program to send -4 to +4 to PORTB
#include <mc9s12dp512.h> // supports PORTB declarations
void main (void)
{
char mynum[ ] = {+1,-1,+2,-2,+3,-3,+4,-4};
unsigned char z;
DDRB = 0xFF; // PORTB is output
for (z=0; z<8; z++)
PORTB = mynum[z];
while(1); // Stay here forever
}

## Slide 11: Unsigned integer
16 bit data type
Range is 0000 – FFFF H
Typically used to define 16 bit variables such as data addresses
Also useful for counter value > 256
Use it sparingly
Use the unsigned variant if negative numbers not expected
C compiler defaults to signed integer

## Slide 12: C program to toggle all bits of PORTB 50,000 times
#include <mc9s12dp512.h> // supports PORTB declarations
void main (void)
{
unsigned int z;
DDRB = 0xFF; // PORTB is output
for (z=0;z<=50000;z++)
{
PORTB = 0x55;
PORTB = 0xAA;
}
while (1); // stay here
}

## Slide 13: Signed integer and other data types
Signed integer
  MSB represents sign where 0 is positive and 1 is negative
  Values include -32,768 thru +32,767
Other types
  Short Long 24 bits
  Long 32 bits
Note the next example

## Slide 14: C program to toggle all bits of PORTB 100,000 times
#include <mc9s12dp512.h> // supports PORTB declarations
void main (void)
{
unsigned long z;
DDRB = 0xFF // PORTB is output
for (z=0; z<=100000; z++)
{
PORTB = 0x55;
PORTB = 0xAA;
}
while (1); // Stay here
}

## Slide 15: Time Delay
2 Ways to create in C language
  Using a loop
  Using HCS12 timers
  See more about timers in Chapter 9
2 factors which affect the accuracy of the delay
  Crystal frequency
  The Compiler that is used
As a result, the actual delay must be tested and adjusted accordingly
Note the following Examples

## Slide 16: C program to toggle PORTB with 250 ms delay assuming 2 MHz clock
#include <mc9s12dp512.h> // supports PORTB declarations
Void MSDelay (unsigned integer);
void main (void)
{
DDRB = 0xFF; // PORTB is output
while (1) // repeat forever
{
PORTB = 0x55;
MSDelay (250);
PORTB = 0xAA;
MSDelay (250);
}
} // continued next slide

## Slide 17: C program to toggle PORTB with 250 ms delay assuming 2 MHz clock continued
void MSDelay (unsigned int itime)
{
unsigned int i; unsigned int j;
for (i=0; i<itime; i++)
for (j=0; j<331; j++);
} // concludes example

## Slide 18: C program to toggle PORTA and PORTB with 250 ms delay assuming 2 MHz clock
#include <mc9s12dp512.h> // supports PORTB declarations
Void MSDelay (unsigned integer);
void main (void)
{
DDRB = 0xFF; // DDRB is output
while (1) // Loop forever
{
PORTA = 0x55;
PORTB = 0x55;
MSDelay (250);
PORTA = 0xFF;
PORTB = 0xFF; // continued next slide

## Slide 19: C program to toggle PORTA and PORTB with 250 ms delay assuming 2 MHz clock cont.
MSDelay (250);
}
}
void MSDelay (unsigned int itime)
{
unsigned int i; unsigned int j;
for (i=0;i<itime;i++)
for (j=0;j<331;j++);
} // end of example

## Slide 20: C program to show the count from 00 to FF H on the LEDs connected to PORTA and PORTB
#include <mc9s12dp512.h>
#define LED PORTA
void MSDelay (unsigned int);
void main (void)
{
DDRB = 0xFF; // PORTB is output
DDRA = 0xFF; // PORTA is output
PORTB = 00; // clear PORTB
LED = 0; //clear PORTA
for (;;) // loop forever
{ // continued on next slide

## Slide 21: C program to show the count from 00 to FF H on the LEDs connected to PORTA and PORTB cont.
PORTB++;
LED++;
MSDelay (500);
}
}
void MSDelay (unsigned int itime)
{
unsigned int i;
unsigned int j;
for (i=0; i<itime;i++)
for (j=0; j<331; j++);
}

## Slide 22: C program to get a byte of data from PORTB then wait ½ second and write it to PORTA, clk = 2MHz
#include <mc9s12dp512.h> // supports PORTB declarations
Void MSDelay (unsigned int);
void main (void)
{
unsigned char mybyte;
DDRB = 0x00; // PORTB is input
DDRA = 0xFF; // PORTA is output
while (1)
{
mybyte = PORTB; // read byte from PORTB
MSDelay (500);
PORTA = mybyte; // send it to PORTA continued on next slide

## Slide 23: C program to get a byte of data from PORTB then wait ½ second and write it to PORTA, clk = 2MHz continued
}
}
void MSDelay (unsigned int itime)
{
unsigned int i;
unsigned int j;
for (i=0; i<itime;i++}
for (j=0;j<331;j++);
}

## Slide 24: C program to read a byte from PORTB, if < 100 send to PORTA else send to PORTK
#include <mc9s12dp512.h> // supports PORTB declarations
Void MSDelay (unsigned int);
void main (void)
{
unsigned char mybyte;
DDRB = 0x00; // PORTB is input
DDRA = 0xFF; // PORTA is output
DDRK = 0xFF; // PORTK is output
while (1)
{
mybyte = PORTB // read from PORTB
// Continued on next slide

## Slide 25: C program to read a byte from PORTB, if < 100 send to PORTA else send to PORTK cont
if (mybyte < 100)
PORTA = mybyte; // first case
else
PORTK = mybyte; // second case
MSDelaty (250); // delay 250 ms
}
}
void MSDelay (unsigned int itime)
{
unsigned int i;
unsigned int j;
for (i=0; i<itime;i++}
for (j=0;j<331;j++);
}

## Slide 26: C program to toggle Port A, B, and K continuously with 250 ms delay, clk is 250 MHz
#include <mc9s12dp512.h> // supports PORTB declarations
Void MSDelay (unsigned int);
void main (void)
{
DDRA = 0xFF;
DDRB = 0xFF;
DDRK = 0xFF; // PORTA, PORTB, & PORTK are output
while (1) // do it forever
{
PORTA = 0x55;
PORTB = 0x55;
PORTK = 0x55; // continued on next page

## Slide 27: C program to toggle Port A, B, and K continuously with 250 ms delay, clk is 250 MHz cont
MSDelay (250); // 250 ms delay
PORTA = 0xAA;
PORTA = 0xAA;
PORTA = 0xAA;
MSDelay (250);
}
}
void MSDelay (unsigned int itime)
{
unsigned int i;
unsigned int j;
for (i=0; i<itime;i++}
for (j=0;j<331;j++);
}