## Slide 1: Section 7.2
Bitwise Logic Operations in C

## Slide 2: Summary of Bit wise operators in C
 |  | AND | OR | EX-OR | INVERTER
A | B | A&B | A¦B | A^B | Y=~B
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1 | 
1 | 1 | 1 | 1 | 0 | 
For example
  0x35 & 0x0F = 0x05 // ANDing
  0x04 | 0x68 = 0x6C // Oring
  0x54 ^ 0x78 = 0x2C // XORing
  ~0x55 = 0xAA // Inverting

## Slide 3: Bit wise shift operators in C
>> shift right
<< shift left
Format
  data >> number of bits to be shifted right
  data << number of bits to be shifted left
For example
  0x9A >> 3 = 0x13 // shifting right 3 times
  0x77 >> 4 = 0x07 // shifting right 4 times
  0x6 << 4 = 0x60 // shifting left 4 times

## Slide 4: C program to operate on Ports A, B, and K using bit wise logical operators
#include <mc9s12dp512.h>
void main (void)
{
DDRA = 0xFF;
DDRB = 0xFF;
DDRK = 0xFF; // Ports A,B, and K are outputs
PORTB = 0x35 & 0x0F; // ANDing
PORTA = 0x04 | 0x68; // Oring
PORTK = 0x54 ^ 0x78; // XORing
PORTA = ~0x55; // Inverting
PORTB = 0x9A >> 3; // Shifting right 3 times
while (1) // stay here
}

## Slide 5: C program to toggle Ports B and A continuously with 250 ms delay
#include <mc9s12dp512.h> // supports PORTB declarations
void MSDelay (unsigned int);
void main (void)
{
DDRA = 0xFF;
DDRB = 0xFF; // Ports A and B are output
PORTA = 0xAA;
PORTB = 0x55;
while (1)
{
PORTA = ~PORTA // continues next slide

## Slide 6: C program to toggle Ports B and A continuously with 250 ms delay cont’d
PORTB = ~PORTB;
MSDelay (250);
}
}
void MSDelay (unsigned int itime)
{
unsigned int i; unsigned int j;
for (i=0; i<itime; i++)
for (j=0; j<331; j++);
} // concludes example

## Slide 7: C program to read PB0 and PB1 and send ASCII character to PORTA accordingly
#include <mc9s12dp512.h>
void main (void)
{
unsigned char z;
DDRB = 0x00; // PORTB is input
DDRA = 0xFF; // PORTA is output
while (1)
{
z = PORTB;
z = z & 0x3; // mask unused bits
switch (z) // now make decision
// continued on next slide

## Slide 8: C program to read PB0 and PB1 and send ASCII character to PORTA accordingly cont’d
{
case (0):
{
PORTA = ‘0’;
break;
}
case (1):
{
PORTA = ‘1’;
break;
}
// continued next slide

## Slide 9: C program to read PB0 and PB1 and send ASCII character to PORTA accordingly cont’d
case (2):
{
PORTA = ‘2’;
break;
}
case (3):
{
PORTA = ‘3’;
break;
}
}
}
} // end of example

## Slide 10: C program to continuously toggle Ports A and B using XOR, 250 ms delay, 2 MHz clock
#include <mc9s12dp512.h> // supports PORTB declarations
void MSDelay (unsigned int);
void main (void)
{
DDRB = 0xFF;
DDRA = 0xFF; // Ports A and B are output
PORTB = 0x55;
PORTA = 0x55;
while (1)
{
// continued next slide

## Slide 11: C program to continuously toggle Ports A and B using XOR, 250 ms delay, 2 MHz clock cont’d
PORTB = PORTB ^ 0xFF; // XOR toggles bits
PORTA = PORTA ^ 0xFF;
MSDelay (250);
}
}
void MSDelay (unsigned int itime)
{
unsigned int i; unsigned int j;
for (i=0; i<itime; i++)
for (j=0; j<331; j++);
} // concludes example