## Slide 1: Section 7.3
Data conversion programs in C

## Slide 2: ASCII code for digits 0-9
Digit | ASCII | Binary | Unpacked BCD
0 | 30 | 0011 0000 | 0000 0000
1 | 31 | 0011 0001 | 0000 0001
2 | 32 | 0011 0010 | 0000 0010
3 | 33 | 0011 0011 | 0000 0011
4 | 34 | 0011 0100 | 0000 0100
5 | 35 | 0011 0101 | 0000 0101
6 | 36 | 0011 0110 | 0000 0110
7 | 37 | 0011 0111 | 0000 0111
8 | 38 | 0011 1000 | 0000 1000
9 | 39 | 0011 1001 | 0000 1001

## Slide 3: Packed BCD to ASCII conversion
Packed BCD | Unpacked BCD | ASCII
0x29 | 0x02, 0x09 | 0x32, 0x39
0010 1001 | 0000 0010, 0000 1001 | 0011 0010, 0011 1001
To convert packed BCD TO ASCII
  First convert to unpacked BCD
  Then convert to ASCII

## Slide 4: ASCII to Packed BCD conversion
Digit | ASCII | Unpacked BCD | Packed BCD
4 | 34 | 0000 0100 | 
7 | 37 | 0000 0111 | 0100 0111
To convert ASCII to packed BCD
  First convert to unpacked BCD to get rid of the 3
  Then combine to make packed BCD
Note the following examples..

## Slide 5: C program to convert packed BCD 0x29 to ASCII and display on Ports A and B
#include <mc9s12dp512.h>
void main(void)
{
unsigned char x, y;
unsigned char mybyte = 0x29
DDRA = 0xFF;
DDRB = 0xFF; // Ports A and B are output
x = mybyte & 0x0F; // Mask upper nibble
PORTB = x | 0x30; // Make it ASCII using OR
y = mybyte & 0xF0; // Mask lower nibble
y = y >> 4; // Shift upper to lower nibble
PORTA = y | 0x30 // Make it ASCII using OR
} // That’s all folks

## Slide 6: C program to convert ASCII digits to packed BCD and display results on PORTB
#include <mc9s12dp512.h>
void main(void)
{
unsigned char bcdbyte;
volatile unsigned char w = ‘4’; // volatile means value may change
volatile unsigned char z = ‘7’;
DDRB = 0xFF; // PORTB is output
w = w & 0x0F; // mask 3
w = w << 4; // Shift to upper nibble to make upper BCD nibble
z =z $ 0x0F; // mask 3
bcdbyte = w | z; // combine to make packed BCD
PORTB = bcdbyte // write to PORTB
}

## Slide 7: Checksum Byte in ROM
Checksum calculation assures ROM data integrity
  Checksum byte is tagged to the end of a series of data
Calculating the Checksum Byte
  Add all bytes together dropping any carry
  Take 2’s compliment of total sum
  This byte shall be tagged to the end of the series
Calculation
  Sum of all bytes including checksum byte must be 0
Note the following examples

## Slide 8: C program to calculate Checksum byte for given data
#include <mc9s12dp512.h>
void main(void)
{
unsigned char mydata[ ] = {0x25, 0x62, 0x3F, 0x52};
unsigned char sum = 0;
unsigned char x;
unsigned char chksumbyte;
DDRA = 0xFF;
DDRB = 0xFF; // Ports A and B are output
// continued for loop on next slide

## Slide 9: C program to calculate Checksum byte for given data cont’d
for (x=0; x<4;x++)
{
PORTA = mydata[x]; // Port A assumes each value of x
sum = sum + mydata[x]; // accumulate the checksum
PORTB = sum; // Port B assumes the value of each sum
}
chksumbyte = ~sum + 1; // 2’s compliment of sum
PORTB = chksumbyte; // write checksum byte to Port B
} // were done milking this
// checksum byte = 0xE8

## Slide 10: C program to perform checksum calculation and write result to Port B
#include <mc9s12dp512.h>
void main(void)
{
unsigned char mydata[ ] = {0x25, 0x62, 0x3F, 0x52, 0xE8};
unsigned char chksum = 0;
unsigned char x;
DDRB = 0xFF; // Port B is output
for (x=0; x<5;x++)
{
chksum = chksum + mydata[x];
}
// continued next slide

## Slide 11: C program to perform checksum calculation and write result to Port B con’t
if (chksum == 0)
PORTB = ‘G’
else
PORTB = ‘B’
}
// That’s all folks

## Slide 12: C program for Binary (Hex FD) to Decimal Conversion
#include <mc9s12dp512.h>
void main(void)
{
unsigned char x, binbyte, d1, d2, d3;
DDRA = 0xFF;
DDRB = 0xFF;
DDRK = 0xFF; // Ports A, B, and K are output
binbyte = 0xFD
x = binbyte / 10
d1 = binbyte % 10 // % operator finds remainder (LSD)
// continued next slide

## Slide 13: C program for Binary (Hex FD) to Decimal Conversion con’t
d2 = x % 10; // middle digit
d3 = x / 10; // most significant digit
PORTA = d1; // display result lsd
PORTB = d2; // display middle digit
PORTK = d3; // display msd
} // snip, snap, snout, this tale is told out