## Slide 1: Section 7.4
I/O bit manipulation and data serialization in C

## Slide 2: C program to toggle bit 5 of PORTB 50,000 times
#include <mc9s12dp512.h>
#define MYBIT PORTB_BIT5 // defined in header file
void main(void)
{
unsigned int z;
DDRB_BIT5 = 1; // bit 5 of Port B is output
for (z=0; z<50000;z++)
{
MYBIT = 1;
MYBIT = 0;
}
while (1) // hang out
} // our work here is done

## Slide 3: C program to toggle bit 0 of Port B without changing any other bits
#include <mc9s12dp512.h>
void main(void)
{
DDRB = DDRB | 0x01; // PB0 is output
while (1)
{
PORTB = PORTB | 0x01 // PB0 is on
PORTB = PORTB & ~0x01 // PBO is off
}
} // Brilliant!

## Slide 4: Bit addressing for HCS12 Ports Using Code Warrior C language
Name | Address (Hex) | X Range
PORTA | PORTA_BITx | 7 >= x >= 0
DDRA | DDRA_BITx | 7 >= x >= 0
PORTB | PORTB_BITx | 7 >= x >= 0
DDRB | DDRB_BITx | 7 >= x >= 0
PORTE | PORTE_BITx | 7 >= x >= 0
DDRE | DDRE_BITx | 7 >= x >= 0
PTH | PTH_PTHx | 7 >= x >= 0
DDRH | DDRH_DDRHx | 7 >= x >= 0
PTJ | PTJ_PTJx | x = 7, 6, 1 or 0
DDRJ | DDRJ_DDRJx | x = 7, 6, 1 or 0

## Slide 5: Bit addressing for HCS12 Ports Using Code Warrior C language con’t
Name | Address (hex) | x Range
PORTK | PORTK_BITx | x = 7 or 5 >= x >=0
DDRK | DDRK_ BITx | x = 7 or 5 >= x >=0
PTM | PTM_PTMx | 7 >= x >= 0
DDRM | DDRM_DDRMx | 7 >= x >= 0
PTP | PTP_PTPx | 7 >= x >= 0
DDRP | DDRP_DDRPx | 7 >= x >= 0
PTS | PTS_PTSx | 7 >= x >= 0
DDRS | DDRS_DDRSx | 7 >= x >= 0
PTT | PTT_PTTx | 7 >= x >= 0
DDRT | DDRT_DDRTx | 7 >= x >= 0

## Slide 6: C program to monitor PA7 and conditionally write to Ports B or K
#include <mc9s12dp512.h>
void main(void)
{
unsigned char x;
DDRA = DDRA & 0x7F; // PA7 is input
DDRB = 0xFF; // PORTB is output
DDRK = 0xFF; // PORTK is output
while (1)
{
x = PORTA & 0x80; // x = 1 if PA7 is high
if (x == 0x80)
PORTB = 0x55;
else
PORTK = 0xAA;
}
}

## Slide 7: C program to monitor PB1 and conditionally write to PA7
#include <mc9s12dp512.h>
Void MSDelay (unsigned int); // We’ve seen this before
#define Dsensor PORTB_BIT1
#define buzzer PORTA_BIT7
void main(void)
{
DDRB_BIT1 = DDRB & ~0x02; // PB1 is input
DDRA_BIT7 = DDRA | 0x80; // PA7 is output
while (1)
{
while (Dsensor == 1)
// continued next slide

## Slide 8: C program to monitor PB1 and conditionally write to PA7 cont’d
{
buzzer = 0;
MSDelay (2);
buzzer = 1;
MSDelay (2);
}
}
}
void MSDelay (unsigned int itime)
{
unsigned int i; unsigned int j;
for (i=0; i<itime; i++)
for (j=0; j<331; j++);
} // concludes example

## Slide 9: C program to monitor enable pin and conditionally write to Port B
#include <mc9s12dp512.h>
#define LCDData PORTB // LCDData declaration
#defube En PORTA_BIT2 // The enable pin
const unsigned char message[ ] = “The earth is but one country”;
unsigned char z;
void main(void)
{
DDRB = 0xFF; // PORTB is output
DDRA = 0b00000100 // PA2 is output, 0b declares binary
for (z=0; z<28; z++) // 28 characters
// continue next slide

## Slide 10: C program to monitor enable pin and conditionally write to Port B
{
LCCData = message [z];
En = 1 // high to
En = 0 // low pulse latches data
}
while (1) // hang out
} // end

## Slide 11: C program to serialize $44 via PB0 LSB first by shifting right
#include <mc9s12dp512.h>
#define PB0 PORTB_BIT0
void main(void)
{
unsigned char conbyte = 0x44;
unsigned char regALSB;
unsigned char x;
regALSB = conbyte;
DDRB_BIT0 = 1; // PBO is output
for (x=0;x<8;x++)
// continued next slide

## Slide 12: C program to serialize $44 via PB0 LSB first by shifting right cont’d
{
PB0 = regALSB & 0x01; // send next bit
regALSB =regASLB >> 1; // shift right 1 bit
}
} // end of program

## Slide 13: C program to serially output $88 MSB first via PB0 by shifting left
#include <mc9s12dp512.h>
#define PB0 PORTB_BIT0
void main(void)
{
unsigned char conbyte = 0x88;
unsigned char regAMSB;
unsigned char x;
regAMSB = conbyte;
DDRB_BIT0 = 1; // PBO is output
for (x=0;x<8;x++)
// continued next slide

## Slide 14: C program to serially output $88 MSB first via PB0 by shifting left cont’d
{
PB0 = (regAMSB >> 7) & 0x01; // send next bit
regAMSB =regASLB << 1; // shift left 1 bit
}
} // end of program

## Slide 15: C program to read a byte from PB0 LSB first and write to Port A
#include <mc9s12dp512.h>
#define PB0 PORTB_BIT0
void main(void)
{
unsigned char temp;
unsigned char REGA = 0;
unsigned char x;
DDRB_BIT0 = 0; // PBO is input
DDRA = 0xFF; // PORTA is output for (x=0;x<8;x++)
// continued next slide

## Slide 16: C program to read a byte from PB0 LSB first and write to Port A cont’d
{
temp = PB0; // read first bit
temp = temp & 0x01; // mask unused bits
temp << 7; // shift left into MSB
REGA = REGA | temp; // give bit value to REGA
REGA = REGA >> 1; // shift right to save
}
PORTA = REGA; // display on Port A
} // end of program

## Slide 17: C program to read a byte from PB0 MSB first and write to Port A
#include <mc9s12dp512.h>
#define PB0 PORTB_BIT0
void main(void)
{
unsigned char temp;
unsigned char REGA = 0;
unsigned char x;
DDRB_BIT0 = 0; // PBO is input
DDRA = 0xFF; // PORTA is output for (x=0;x<8;x++)
// continued next slide

## Slide 18: C program to read a byte from PB0 MSB first and write to Port A cont’d
{
temp = PB0; // read first bit
temp = temp & 0x01; // mask unused bits
REGA = REGA | temp; // give bit value to REGA
REGA = REGA << 1; // shift left to save
}
PORTA = REGA; // display on Port A
} // end of program