## Slide 1: Section 7.5
Program ROM allocation in C

## Slide 2: RAM vs ROM data space
Several Kbytes of data RAM
  Read or write directly or indirectly
Several hundred Kbytes of program space
  Opcodes are directly under control of PC register
  We already learned how to access using indexed addressing mode in Chapter 6
  Some applications will have trade off between code storage and fixed data (eg look up table)
  Next we look how to do this in C

## Slide 3: Allocating Program Space to Data
The const keyword
  Eg. const char mynum[ ] = “Hello”;
// example of using program space for data storage
#include <mc9s12dp512.h>
const char mynum[ ] = “0123456789”;
void main(void)
{
unsigned char z;
DDRB = 0xFF;
for (z=0;z<10;z++)
PORTB = mynum[z];
}

## Slide 4: Allocating Program Space to Data using @ to store at specific address
// example using @ directive
#include <mc9s12dp512.h>
const char message[ ] @ 0xD200 = “Hello”
void main(void)
{
unsigned char z;
DDRB = 0xFF // DDRB is output
for (z=0;z<5;z++)
PORTB = message[z];
}

## Slide 5: Let’s Discuss the following
#include <mc9s12dp512.h>
void main (void)
{
DDRB = 0xFF;
PORTB = ‘H’;
PORTB = ‘E’;
PORTB = ‘L’;
PORTB = ‘L’;
PORTB = ‘O’
}
// ADVANTAGES?
// DISADVANTAGES?

## Slide 6: How about this one?
#include <mc9s12dp512.h>
void main(void)
{
unsigned char z;
unsigned char mydata[ ] = “HELLO”;
DDRB = 0xFF // PORTB is output
for (z=0;z<5;z++)
PORTB = mydata[x];
}
// advantages?
// what could be done better?
// where is the data stored?

## Slide 7: Yet another one
#include <mc9s12dp512.h>
const char message[ ] = “HELLO”
void main(void)
{
unsigned char z;
DDRB = 0xFF; // PORTB is output
for (z=0;z<5;z++)
PORTB = message[z];
}
// advantages?
// where is the data stored?