## Slide 1: Section 6-4
MACROS and MODULES

## Slide 2: What is Macro and How is it Used?
Used to accomplish a repetitive task
  Reduces time spent programming and reduces errors
Macro Definition
  3 parts
    Name MACRO
    body
    ENDM
May be invoked by name after it is defined
Parameters are labeled with / followed by 0 – 9 or letter
Parameters are arguments passed to Macro

## Slide 3: Macro Examples
MOVE MACRO
LDAA #\1
STAA \2
ENDM
; 3 WAYS TO USE
MOVE $55 $820 ; SENDS 55 H TO LOCATION 820
VAL1 EQU EQU $55
RAMLOC EQU $820
MOVE VAL1, RAMLOC
3. MOVE $55, PORTB ; SENDS 55H TO PORTB

## Slide 4: Using Local Labels in a Macro
These must be preceded with \@
EG macro for a time delay
DELAY1 MACRO
LDAA #\1
STAA \2
\@BACK NOP
NOP
DEC \2
BNE \@BACK
ENDM

## Slide 5: Toggle PORTB using Macros
; Toggling Port B using a macro
; sending data
MOVE: MACRO
LDAA #\1
STAA \2
ENDM
; time delay
Delay1: MACRO NOP
NOP
NOP
NOP
; CONTINUED NEXT SLIDE

## Slide 6: Toggle Port B continued
DEC \2
BNE \@BACK
ENDM
; Toggling Port B in main
BSET PORTB, %11111111 ; PORT B IS OUTPUT
OVER MOVE $55, PORTB
DELAY1 200, $810
MOVE $AA, PORTB
BRA OVER
END

## Slide 7: INCLUDE directive
Save macros in file with .mac extension
Including that file name will make the macros available to the .asm file
If the .mac file were named mymacro.mac
include ‘mymacro.mac ; get macros from macro file

## Slide 8: MLIST directive
When viewing the list file..
  Macros are fully displayed by default
If this is cumbersome because of extensive macro use..
  We can disable viewing macros using MLIST OFF
  We can enable viewing macros using MLIST ON

## Slide 9: Macros vs Subroutines
Macros increase Code size each time they are called
Subroutines do not
  These use stack space when called
  Can lead to problems when there is a nested call (One subroutine calling another)
    This can lead to a stack overflow causing the program to crash

## Slide 10: Modules
It is common practice to break a software project into small modules and distribute them among several programmers
This has the advantage of making the project more manageable as well as
  Each module may written, debugged, and tested individually
  Failure of one module does not hold up entire project
  Problem identification is easier
  Modules can link with high level languages such as C
  This approach shortens project implementation interval

## Slide 11: Writing Modules
This is basically a subroutine with a unique filename
Linking them together is done using…
  XREF directive (External Reference)
  XDEF directive (External Define)
XREF (EXTERNAL) directive
  Notifies linker that certain names and variables may be defined outside of the present module
  Each name may use a separate XREF call out or many could be listed with 1
XDEF (GLOBAL) directive
  Must be included in the module to match each XREF directive

## Slide 12: XREF and XDEF example
; Main program to calculate and test checksum byte, first some bookkeeping
XREF CALCHKSUM
XREF TSTCHKSUM
XDEF MYRAM
XDEF COUNTREG
XDEF CNTVAL
XDEF CNTVAL1
MYRAM EQU $860
COUNTREG EQU $820 ; RAM LOC FOR COUNTER
CNTVAL EQU 4 ; VALUE FOR ADDING 4 BYTES
CNTVAL1 EQU 5 ; VALUE FOR ADDING 5 BYTES
; CONTINUED NEXT

## Slide 13: XREF and XDEF example continued
; Main
LDS #$900 ; INITIALYZE STACK
JSR COPYDATA ; THIS SUBROUTINE IS INTERNAL
JSR CALCHKSUM ; THIS SUBROUTINE IS EXTERNAL
JSR TSTCHKSUM ; THIS SUBROUTINE IS EXTERNAL
BRA $ ; HANG OUT HERE
; Continued next slide

## Slide 14: XREF and XDEF example continued
; Subroutine to copy data
COPYDATA
LDX #MYBYTE ; X POINTS TO $8500
LDY #MYRAM ; Y POINTS TO $860
LDAA #COUNTVAL ; A = 4
STAA COUNTREG ; COUNTER INITIALYZED TO 4
B1 LDAA 1,X+ ; GET ROM DATA AND INCREMENT POINTER
STAA 1,Y+ ; STORE IN RAM AND INCREMENT POINTER
DEC COUNTREG ; DECREMENT COUNTER
BNE B1 ; LOOP UNTIL 0
RTS ; RETURN TO CALLING PROGRAM
; Continued next slide

## Slide 15: XREF and XDEF Continued
; last minute details
ORG $8500
MYBYTE FCB $25, $62, $3F, $52, $00
END
; External subroutines next

## Slide 16: XREF and XDEF Continued
; calculating the check sum an external reference to main
XREF MYRAM
XREF CNTVAL
XREF CNTVAL1
XREF COUNTREG
XDEF CALCHKSUM
CALCHKSUM
LDAA #CNTVAL ; A = 4
STAA COUNTREG ; COUNTER INITIALYZED
LDX #MYRAM ; LOAD POINTER FROM RAM ADDERSS
CLRA ; A = 0
; CONTINUED NEXT

## Slide 17: XREF and XDEF Continued
; continuing calchksum routine
B2 ADDA 1,X+ ; ADD VALUE FROM MYRAM AND INCREMENT
DEC COUNTREG ; DECREMENT COUNTER
BNE B2 ; LOOP COUNTER NOT 0
NEGA ; TWO’S COMPLIMENT SUM
STAA 0,X ; SAVE CHECKSUM AS LAST BYTE
RTS ; RETURN TO CALLING PROGRAM
END
; Testing checksum next slide

## Slide 18: XREF and XDEF Continued
; testing checksum
INCLUDE ‘mc9s12dp512.inc’
XREF MYRAM
XREF COUNTREG
XREF CNTVAL
XREF CNTVAL1
XDEF TSTCHKSUM
TSTCHKSUM
BSET DDRG, %11111111
LDAA CNTVAL+1 ; ADDING 5 BYTES INCLUDING CHECKSUM
STAA COUNTREG ; INITIALYZE COUNTER
;CONTINUED NEXT

## Slide 19: XREF and XDEF Continued
; test checksum continued
LDX #MYRAM ; LOAD POINTER FROM RAM ADDRESS
CLRA ; A = 0
B3 ADDA 1, X+ ; ADD AND INCREMENT POINTER
DEC COUNTREG ; DECREMENT COUNTER
BNE B3 ; LOOP UNTIL COUNTER IS 0
CMPA #0 ; COMPARE A TO 0
BEQ G1 ; IF 0 THEN BRANCH
LDAA #’B’ ; ELSE BAD
STAA PORTB ; STORE RESULT
RTS ; RETURN TO CALLING PROGRAM
; GOOD RESULT NEXT SLIDE

## Slide 20: XREF and XDEF Continued
; IF THE CHECKSUM IS GOOD
G1 LDAA #’G’ ; A = ASCII G
STAA PORTB ; STORE RESULT
RTS ; RETURN TO CALLING PROGRAM
END

## Slide 21: Linking modules in Code Warrior
This is accomplished by copying the related .asm files into the source folder in code warrior.