## Slide 1: Section 0.5
Risc Architicture

## Slide 2: Ways to increase CPU power
Increase Clock Speed
  Increased power consumption and heat dissipation
  This is a problem for handheld devices
Use Harvard Architecture
  Used on single chip microcontrollers
Use a RISC Architecture
  Note the following slides

## Slide 3: Traditional Approach and RISC feature 1
Include as many instructions as possible into CPU
  Some of these performed complex tasks
  Referred to as CISC (complex instruction set computers)
Instructions could be between 1 and 3 bytes.
  CLRA – a 1 byte instruction to clear the accumulator
  ADDA #mybyte – a 2 byte instruction to add “mybyte” to the accumulator
  JMP target_address – a 3 byte instruction to Jump
This makes the instruction decoder complicated
This may be simplified by using standard sized instruction sizes
This is the first feature of RISC architectures

## Slide 4: Feature 2 – Large number of registers
At least 32
Advantage is that a large stack is not needed to store parameters
This is achieved by a 512 byte Ram Space in HCS12 microcontrollers

## Slide 5: Feature 3 RISC
Small instruction set
  ADD, SUB, MUL, LOAD, STORE, AND, OR, EXOR, CALL, JUMP….
  This makes Assembly language programming difficult compared to CISC
  But, useful in high level programming environments such as C
  Leads to large programs requiring more memory
  Result of availability of cheap memory
  Before semiconductor memory CISC architecture more efficient

## Slide 6: Feature 4 RISC
95% of all instructions in a RISC processor may processed in one clock cycle
Some of the remaining 5% may be processed in one clock cycle by code scheduling, a job of the compiler
This is the most important characteristic of a RISC Architecture

## Slide 7: Feature 5 RISC
CISC instructions may consume 40 to 60% of the CPU transistors
RISC instructions are hard wired and require no more than 10% of the CPU transistors

## Slide 8: Feature 6 RISC
RISC uses load/store
CISC
  Data may be manipulated while still in memory then moved back to external memory, sometimes resulting in delay
RISC
  Instructions can only load data from or store data into external data locations
  Both operands are brought into registers then the logic or arithmetic operation is performed before the result is stored in external memory
  First use on the Cray 1 super computer in 1976
  Brought into forefront by David Patterson of Berkely
  Some RISC concepts used in x86 processors to enhance competitiveness