## Slide 1: Semiconductor Memory
Section 0-3

## Slide 2: Some terminology
Bit 0
Nibble 0000
Byte 0000 0000
Word 0000 0000 0000 0000
Kilobyte 1024 bytes = 2^10 bytes
Megabyte 1048576 bytes = 2^20 bytes
Gigabyte = 2^30 bytes
Terabyte = 2^40 bytes

## Slide 3: Internal Organization of computers
3 major subsystems
  CPU – Central Processing Unit
  Memory
  I/O Input Output
Connected by buses
  Data
  Address
  Control

## Slide 4: Computer Block Diagram
CPU
RAM
ROM
Printer
Disk
Mon
Keyboard
Address Bus
Data Bus
Control Buses (MEMR, MEMW, IORD, IOWR)

## Slide 5: More About the Data Bus
Analogous to Highway
  The more lanes, the more simultaneous traffic
The more data buses the better
  This adds to expense
Note that we currently have 64 bit CPUs and operating systems
The size of the data bus is related to both size and precisions of arithmetic operations

## Slide 6: More About the Address Bus
Every addressable device must have a unique address
The larger the address bus, the larger number of devices which may be addressed by the CPU
Recall that decoders are used on addressable device to establish their address.
The number of devices which may be addressed is always equal to 2^x where x is the number of address lines.
For example, a 16 bit address bus can access 64k of addressable memory
This is a unidirectional bus (send only from CPU)

## Slide 7: Relation of CPU to RAM and ROM
The CPU processes information that is stored in Memory
  ROM (Read Only Memory) stores information that is fixed and permanent
    Information Tables
    Essential Programs
  RAM (Random Access Memory) stores temporary information which may change over time.
    Application Programs
    Operating Systems
  This information is accessed from memory because accessing the disk is too slow.
    The CPU tries to access RAM and ROM first (primary memory)
    Disk Second (Secondary Memory) to transfer to RAM

## Slide 8: Memory Capacity
This is the number of bits a memory chip can store
Chip capacity has units of bits, Computer system capacity has units of bytes

## Slide 9: Memory Organization
Memory chips are organized into a number of locations within the IC
Each location can hold 1, 4, 8, 16, or more bits
  The number of bits that each location will hold is equal to the number of data pins on the chip.
  The number of locations on the chip is determined by the number of address pins on the chip say x. 2^x is the number of locations (addresses) on the chip
Total number of bits which may be stored on the entire chip is given by 2^(address pins) times the number of data pins

## Slide 10: Organization/Capacity Example
A particular memory chip has 16 address pins and 8 data pins
  Organization: 2^16 locations of 8 bits 64K x 8
  Capacity: 2^16 * 8 131072 bits

## Slide 11: Another Organization/Capacity Example
We have a chip with 256k capacity with 8 data pins.
  The organization is 256k/8 = 32K x 8
  The number of address lines is 15 since 2^15 = 32K

## Slide 12: Need for Speed
This is one of the most important aspects of a memory chip
Accessing the data:
  Present address
  Enable read pin
  Delay
  Data available
The delay is the chips access time or speed
Higher speed is typically more expensive than lower speed

## Slide 13: ROM (read only memory)
Does not lose its contents on loss of power
Also called nonvolatile memory
Different types such as:
  PROM
  EPROM
  EEPROM
  FLASH EPROM
  MASK PROM

## Slide 14: PROM (programmable ROM) and OTP
This is the type of ROM that the user can burn information into
  Programmable by user
  A fuse exists for each bit in the PROM
  Programming consists of blowing the fuse.
  This act may not be changed once accomplished so it is also called One Time Programmable OTP
  Burning the Rom requires special equipment called a ROM burner or ROM programmer

## Slide 15: EPROM (erasable programmable ROM) and UV-EPROM
Different than OTP in that a particular chip may be programmed on the order of a thousand times.
Useful in development activities where changes are usually encountered.
UV-EPROM is a widely used technology where ultra violet radiation is exposed to the device through a window on the chip to erase is contents, which takes about 20 minutes to accomplish.
To program a UV-EPROM
  Erase the chip. (Even if it is new)
  Program the chip using the ROM burner
  Replace the chip into the system socket

## Slide 16: Some UV-EPROM Memory Chips
For example, 27C256-15 is CMOS, with 256k capacity with 15 ns
access, and 32k x 8 organization.

## Slide 17: 27xx ROM family pin outs

## Slide 18: Example of 27xx pins comprehension
Find the number of address and pins on 27256 ROM.
  27256 has capacity of 256k and 32k x 8 organization
    Note that all ROMs have 8 data pins
    Thus there are 15 address pins (2^15 = 32K)
Note the previous slide to confirm A0 thru A14

## Slide 19: EEPROM (electrically erasable programmable ROM)
Advantages compared to EPROM
  Method of erasure is instantaneous.
  Can selectively erase bytes
Disadvantages compared to EPROM
  Additional programming circuity required on system board
  Cost per bit is much higher

## Slide 20: Flash Memory EPROM
Method of erasure is electrical
  Takes less than a second to erase
  Contents may be erased block by block
  Widely used to update BIOS ROM of the PC
  As of 2015, most solid state drives used nand gate based flash memory
  Access time of Flash Memory is on the order of 100 ns

## Slide 21: Mask ROM
Contents are programmed by manufacturer
Not user programmable
Mask refers to a fabrication step
Costly Process
  Requires high volume
  Requires extremely low risk of change
  Results in low variable cost per device
Conforms to 8 data pin standard for ROM

## Slide 22: Ram (random access memory)
This is referred to as volatile memory because it loses data when it loses power. Also know as RAWM (read and write) memory
3 types
  Static RAM
  Nonvolatile RAM
  Dynamic Ram

## Slide 23: SRAM (static RAM)
The storage cells are made up of flip-flops and thus do not require refreshing to keep their data,
  This a key advantage of SRAM
On the other hand,
  Two many transistors are required for implementation which make this type of memory lower in capacity compared to other technologies.

## Slide 24: 2k x 8 SRAM pin out and block diagrams

## Slide 25: 6116 SRAM Block Diagram

## Slide 26: Steps required to write data into SRAM
Provide the addresses into pins A0 – A10
Activate the CS pin
Make WE = 0 while RD = 1
Provide data to IO0 to IO7
Make WE = 1 and data will be written on the positive edge of the WE signal

## Slide 27: Steps required to read data from SRAM
Provide the addresses to pins A0 – A10
  This is the start of the access time
Activate the CS pin
While WE = 1 a high to low pulse on the OE pin will read the data out of the chip

## Slide 28: NV-RAM (nonvolatile RAM)
This type of RAM retains its contents when the power is lost.
  It does this by using an internal lithium battery as a back up power supply
  This accomplished by control circuitry on each chip to detect a drop in Vcc
  It can retain its info for up to 10 years
  SRAM cells are made from CMOS which has very low power consumption
  One can read it or write to it in the same way as SRAM
  It is very expensive comparatively as far as cost per bit is concerned

## Slide 29: Some SRAM and NV-RAM examples

## Slide 30: DRAM (dynamic RAM)
Computer designers have needed large amounts of inexpensive read/write memory since the original computers were developed
In 1970 Intel introduced the first dynamic ram
  Its density was 1k bits
  It used a capacitor to store each bit
    Use of capacitor is simpler than groups of transistors
    But this requires the data to be refreshed due to leakage currents

## Slide 31: DRAM (dynamic RAM) Pros and Cons
Advantages
  High Density
  Lower Cost per bit
  Lower Power Consumption per bit
  Large capacities of 2 Gigabit and more are now common
Disadvantages
  Memory must be periodically refreshed
  Memory can not be accessed during refresh operation

## Slide 32: DRAM Packaging
It is difficult to keep a reasonable number of pins in the face of large capacity DRAMs
As a result multiplexing and demultiplexing is used to reduce required pin count
  One method of accomplishing this is to split the address in half and send each half through the same pins
  The first half is referred to as the row, and the second half is referred to as the column
  In the case of 64K x 1 organization the RAS is activated to latch the first 8 bits of the address, then the CAS is activated to latch the second 8 bits or octet
  In order to reduce complexity, many small capacity microcontroller projects will use SRAM or NV-RAM instead of DRAM

## Slide 33: DRAM organization
May be x1, x4, x8, or x16
Data pins may be also called I/O
Note the below example of 256k x 1 DRAM with pins A0 – A8, RAS, CAS, Data in, Data Out, Vcc, and Ground.

## Slide 34: Example DRAM Memory Chips

## Slide 35: Comparison of DRAM and SRAM
Consider an organization of 16k by 4
  Recall that 2^14 = 16k
DRAM
  7 address pins (A0 – A6)
  2 pins for RAS and CAS
  4 pins data bus
SRAM
  14 address pins (A0 – A13)
  No RAS or CAS
  4 pins data bus

## Slide 36: Memory Address Decoding
Consider an SRAM..
  These will have a CS (chip select) or CE (chip enable) pin
Connecting to CPU
  Data bus is connected directly
  Control Signals RD (read) and WR (write) are respectively connected to the OE (output enable) and WE (write enable) pins of the memory device
  For address buses, the lower bits of the address bus go directly to the address pins on the device, but the higher ones are used to activate the CS pin via decoding logic.
Normally the CS pin is active low and memories are divided into blocks. The output of the decoder selects a given block

## Slide 37: Memory Block Selection
Simple Logic Gates
Using 74LS138
Programmable Logic such as CPLD or FPGA

## Slide 38: Simple Logic Gate Address Decoder
The simplest method is to us a NAND gate decoder..
  The out put of a NAND gate is active low.
  Most Chip Select Pins are Active Low
  If the CS pin is active high, an AND gate will be used instead
  Any address range may be decode using the right combination of NAND gates and inverters
Note the example on the next slide
  0011 on A12 – A15 will select the chip (Hex 3)
  0000 0000 0000 on A0 – A11 results in hex 3000
  1111 1111 1111 on A0 – A11 results in hex 3FFF

## Slide 39: Simple Logic Address Decoder

## Slide 40: Using the 74LS138 3 – 8 decoder
One of the most widely used decoders
3 inputs A, B, and C generate 8 active low outputs Y0 to Y7,
Each output is connected to CS of a different memory device allowing control of 8 memory blocks
Three additional inputs G1, G2A, and G2B may connected to an Address or Control Signal
  G2A and G2B active low
  G1 active high
  These inputs must be terminated in way or another
  These inputs enable the device

## Slide 41: 74LS138 pin out, function table, and schematic

## Slide 42: 74LS138 Example
What is the address range for Y5 in the previous slide?
  A15 must be O for decoder to be activated since it is connected to G2A
  C, B, and A are 101
  The rest are either all 0 (low boundary) or all 1 (high boudary)..
  0101 0000 0000 0000 or hex 5000 to 0101 1111 1111 1111 or hex 5FFF

## Slide 43: Using Programmable Logic as Address Decoder
Devices include PAL, GAL, and FPGA
Advantages
  May be programmed for any combination of addresses
  Very versatile
  More inputs available
Disadvantages
  Additional Software Required
  Additional Burner Required