## Slide 1: Section 0.4
Harvard and von Neumann CPU Architectures

## Slide 2: Inside the CPU
Programs stored in memory provide instructions to perform a task..
The CPU uses the following resources to complete its function of fetching and executing programs.
  Registers – registers temporarily store information in 8 bit or larger registers.
    The larger the register size, the better the CPU albeit at an increased cost
  ARU – Arithmetic/Logic Unit
    Performs arithmetic and logic functions
  Program Counter – Points to the next program instruction
    In the x86 architecture this is implemented as an IP or Instruction Pointer register
  Instruction Decoder – Stores the meaning of all possible instructions and the appropriate CPU steps required.

## Slide 3: Internal CPU operation
Consider a CPU with 16 bit address and 8 bit data buses, 4 registers (A – D), accessing addresses 0000 to FFFF hex.
The required operation is to add 3 hexadecimal numbers (21,42, and 12 hex) consisting of the following steps, instruction code and data:
  Move value 21 into register A, code B0, data 21
  Add value 42 to register A, code 04, data 42
  Add value 12 to register A, code 04, data 12
  Halt, code F4

## Slide 4: Resulting Memory Contents
Assume that the program counter is set to 1400 then we would see the following memory contents.
  1400 – B0 (move to register A)
  1401 – 21 (data)
  1402 – 04 (add to register A)
  1403 – 42 (data)
  1404 – 04 (add to register A)
  1405 – 12 (data)
  1406 – F4 (halt)

## Slide 5: Comparison von Nuemann vs Harvard
Von Nuemann
Harvard
Address Bus
Data Bus
CPU
Code Memory
Data
Memory
Data
Memory
CPU
Code Memory
Address Bus
Address Bus
Data Bus
Data Bus

## Slide 6: Von Nuemann and Harvard Comparison.
Von Nuemann shares same bus to access code and data an early architecture
  Developed at Princeton
Harvard uses separate buses to access code and data
  This will double the number of traces on the mother board.
  For this reason it is not used in PC’s or other workstations.
  Developed at Harvard
In some cases Harvard Architecture is used internally and von Nuemann Architecture for external code and data memory
  Eg. PIC