## Slide 1: EET 845 01
Chapter 0

## Slide 2: Numbering and Coding Systems
  Human numerical system
  Base 10
Computer Numerical System
  Base 2
  Hexadecimal Base 16
  ASCII
    Binary format of alphanumeric code

## Slide 3: Decimal and Binary Number Systems
Base 10 based upon the number of digits (get it) humans have.
Base 2 based upon output state of transistor switch
  These 2 binary levels referred to as bits

## Slide 4: Converting from decimal to binary
One method is to deconstruct the decimal number into descending powers of 2.
  Look at an example say 39.
  What is the highest power of 2 <= 39?
  Answer 2^5 = 32 remainder 7 => 2^4 and 2^3 bits are 0
  What is the highest power of 2 <= 7
  Answer 2^2 = 4 remainder 3
  Next answer 2^1 = 2 remainder 1
  Next answer 2^0 = 1
  Result: 100111

## Slide 5: Converting from Binary to Decimal
The basic method is to multiply each bit in the binary number by its associated power of two. The LSB starts at 2^0, the next is 2^1 and so on.
  Consider our previous example 100111 base 2..
  LSB.. 1*1 = 1
  Plus 1*2 = 2
  Plus 1*4 = 4
  Plus 0*8 = 0
  Plus 0*16 = 0
  Plus 1*32 = 32
  Result: 39 base 10

## Slide 6: Consider an 8 bit word..
We can write the power of two above each bit of the word from MSB of 2^7 to LSB of 2^0 and work this in a more intuitive fashion.
  Consider the number 135..
  What is the Highest number which can be stored in an 8 bit word?
  128+64+32+16+8+4+2+1 = 255! All Red..
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 0 | 0 | 1 | 1 | 1
7 |  |  |  |  | 3 | 1 | 0

## Slide 7: Counting in Decimal
Lowest digit.. 0
Highest digit .. 9
As we pass the highest digit we increment to a power of ten
In the case of 10 this 1*10^1 + 0
For example 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16.

## Slide 8: Counting in Binary
Lowest digit is 0
Highest digit is 1
Each time we pass the highest digit we increment a power of 2.
For Example, 0, 1, 10, 11, 100, 101, 110, 111, 1000, 1001, 1010, 1011, 1100, 1101, 1110, 1111, 10000

## Slide 9: Counting in Hexadecimal
Digits: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Count to 16:
  1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F, 10 where 10 => 16^1
  Why would we have such a thing?
    Convenient way to note the contents of a 16 bit word.

## Slide 10: Adding and Subtracting Binary Numbers
To add, remember that 1 + 1 = 10
  1101 + 1011 = 10110
To subtract, take the two’s complement of the quantity to be subtracted and add it to the number which is to be subtracted from.
  Two’s complement is two steps.
  First invert the number (reverse 1 to 0, and 0 to 1) 1101 becomes 0010
  Then add one to the result.. 0010 becomes 0011
Consider 1111 – 1101.. (This is 15 -13 in base 10)
  1111 + 0011 = 10010 ; Discard the overflow MSB which results in 0010

## Slide 11: Adding Hexadecimal Numbers
Start with the Least significant digit
Add the two least significant together
  If the result is less than 16, carry the number to the result
  If the result is greater than 16, subtract 16 from it then carry the number to the result also carry a 1 to the next significant digit.
  Proceed until done with most significant digit.
Example: 24E7 + 18F9
  7 + 9 = 16 => 0 carry 1
  1 + E + F = 30 => E carry 1
  1 + 4 + 8 = 13 => D
  2 + 1 = 3 => 3
  Result: 3DE0

## Slide 12: Subtracting Hexadecimal Numbers
Works pretty much like subtraction of base 10 numbers except we are borrowing 16 instead of 10 from the next significant digit.
Consider the previous numbers. Subtract 18F9 from 24E7
  Least significant digit.. (7+16)-9 = E
  Next digit (16’s).. (D+16)-F = E
  Next digit (16^2’s).. (3+16)-8 = B
  Next digit (16^3’s).. (1-1) =0
  Result: BEE

## Slide 14: ASCII Code
Acronym stands for American Standard Code for Information Exchange
Hex 41 – 5A are the 26 capital letters
Hex 61 – 7A are the 26 lowercase letter
Hex 30 – 39 represent 0 - 9