## Slide 1: Chapter 1
The HCS12/9S12 Microcontroller:
History and Features

## Slide 2: Chapter Objectives
Upon completion you will be able to:
Compare and Contrast Microprocessors and Microcontrollers
Describe advantages of Microcontrollers for some applications
Explain the concept of embedded systems
Discuss criteria for considering a microcontroller
Explain the variations of speed, packaging, memory and cost per unit, and how these affect choosing a microcontroller
Explain the evolution of 68xx microcontrollers
Compare and contrast the various members of the HCS12 family
Give the history and features of HCS12/9CS12 microcontrollers

## Slide 3: Section 1.1 Microcontrollers and Embedded Processors
What is the difference between Microcontrollers and General Purpose Microproccesors?
  Example of general purpose microproccesor
    Intel x86 – 8086,80286 to pentium
    Motorola Power PC
Microprocessors require external resources such as
  RAM, ROM, I/O, Timers
These are all included on a single chip in a Microcontroller

## Slide 4: Microprocessor vs. Microcontroller

## Slide 5: Microcontrollers for embedded systems
An embedded product is controlled by its own internal microprocessor or microcontroller as opposed to an external controller
  In an embedded system, typically the microcontrollers ROM is burned with specific functions needed for the system
    Consider a printer for example: The microcontroller for the printer mainly needs to get the data from the print server and print it.
    As opposed a PC which can be used for any number of applications
    Typically only one application software is burned into an embedded system
    Some PC peripherals could contain embedded systems

## Slide 6: In Class Exercise
Let’s brainstorm a list of products in our every day life that contain embedded systems.

## Slide 7: Microprocessor Embedded Systems
Some times we need more computing power for high end embedded systems
  We might consider
    X86
    Power PC
    ARM
    Single Chip Computer
  X86 has advantage due to standardization of DOS, Windows and Linux
    Shortened development time
    Reduced cost

## Slide 8: Choosing a Microcontroller
5 major options
  Freescale 68HC08, 68HC11, 68HC12
  Intel 8051
  Atmel AVR
  Zilog Z8
  Microchip Technology PIC
Each option has unique instruction set and may have different bus structures 16 or 32 bit

## Slide 9: Criterion for Application Choice
Meeting the computing need of the product requirements cost effectively
Availability of development tools
Wide availability and reliable sources for procurement

## Slide 10: Meeting the Product Computing Need
8, 16, 32 bit architecture?
Speed (Clock Rate)
Packaging – DIP, QFP
  Product process
  Prototyping
Power Consumption
Memory Capacity – RAM, ROM
I/O pins and timer
Upgrade Path
Cost per unit

## Slide 11: Development Tool Availability
Availability of
  Assembler
  Debugger
  Code efficient C language compiler
  Emulator
  Tools
  Technical Support
  In house and External expertise

## Slide 12: Supply Chain Issues
Availability of needed quantities now and in the future.
  Product obsolesence
  8051 has largest number of diversified suppliers, more than 50
  Freescale, Atmel, Zilog and Microchip Technology have dedicated large support for their microcontrollers to ensure availability because they are mature, stable and single source
  FPGA chips and ASIC libraries are available to support these microcontrollers

## Slide 13: Mechatronics and Microcontrollers
Microcontrollers are playing an increasing role
Mechatronics is about integration of mechanics, electronics and information processing
Mechatronics requires multidisciplinary expertise across disciplines such as mechanical engineering, electronics, information technology, and decision making theories