## Slide 1: Chapter 2
HCS12 ARCHITECTURE AND ASSEMBLY LANGUAGE PROGRAMMING

## Slide 2: Chapter Objectives
Upon completion, you will be able to
  List the registers of the HCS12
  Manipulate data using the registers with load and add instructions
  Code simple HCS12 Assembly language instructions
  Assemble and Run an HCS12 program
  Describe the sequence of events that occur upon power up
  Examine Programs in ROM code
  Explain the ROM memory map
  Detail the execution of Assembly language instructions
  Describe addressing modes
  Describe directives for Assembly language programming
  Explain the purpose of the condition code register
  Discuss memory space allocation
  Diagram the use of the stack

## Slide 3: Section 2.1 Inside the HCS12
Registers
  Temporarily store data
  Most widely used
    A 8 bit accumlator
    B 8 bit accumulator
    X index register
    Y index register
    SP stack pointer
    CCR condition code register
    A and B may be combined to yield a 16 bit register called D

## Slide 4: Load Instructions
LDAA source ; copy source to register A
  Source could be immediate or a value in memory
  LDAA #$35 ; loads 55 hex into Accumulator A
    # signifies an immediate value
    $ signifies that the immediate value is base 16
  LDAB #$21 ; loads 21 hex into Accumulator B
  ABA ; add contents of B to A
    Register A contents becomes 76 hex
    Register B remains at 21 hex

## Slide 5: Caveat Scholaticus
Values may be loaded into registers A, B, X, Y, and SP
  Immediate value must be denoted with # sign
  $ sign denotes a hex value
  % sign denotes a binary value
  Absence of sign denotes decimal
  Loading hex values between 0 and F will result in higher significant bits defaulting to 0
  Loading a too large of a value into a register will result in an error
  Absence of the # sign indicates that the value should be loaded from a memory location
    Eg LDAA $17 will load the contents of memory location 17 hex

## Slide 6: ADDA and ADDB
ADDA source ; add source operand to accu A
  Result is stored in A
ADDB source ; add source operand to accu B
  Result is stored in B
Example
  LDAA #$25 ; load 25 hex to A
  LDAB #$34 ; load 34 hex to B
  ABA ; add B to A and store result in A
In two lines,
  LDAA #$25 ; load 25 hex into A
  ADDA #$34 ; add 34 hex into A and store result in A
  In this case the 34 hex operand is called an immediate operand