## Slide 1: Chapter 2 Section 2
The HCS12 Memory Map

## Slide 2: Memory Space Allocation in the HCS12
The HCS12 has 64 Kbytes of directly accessible memory space as follow:
  Register Space
    Dedicated to I/O and Special Function Registers (SFR) such as timers, serial communication, ADC, etc.
    I/O and SF registers are 8 bit
    The amount assigned may vary widely from chip to chip even among members of the same family.
      Sometimes a small as 64 bytes
      Addresses start at 0000

## Slide 3: Partial List of MCHC9I2B32 Register Addresses

## Slide 4: Data RAM Space
Capacity ranges from 128 bytes to several KB
  Used for data variables, scratch pad and stack
  Accessed by microcontroller instructions
  This is Read/Write memory
  Larger sizes will result in more difficulty on the programmers part in managing the RAM locations if programming in assembly language
  Use of C compilers will simplify this, and this the reason that we need the larger RAM capacities.
  The RAM has a byte size width
  Please contain your excitement until section 2.8

## Slide 5: MC9S12Dx256 Memory Allocation

## Slide 6: EEPROM Space
Range of 128 to several thousand bytes
  Varies widely from chip to chip
  Sometimes used for code storage
  Most often used for storage of critical data

## Slide 7: Code ROM Space
Capacity ranges from a few to several hundred KB
  Used for program storage
  Usually in Flash memory
  Under control of the program counter (PC)
  Might also be used for storage of static data such as ASCII data strings
  ROM greater than 64K will be accessed by page swapping

## Slide 8: HCS12 Memory Allocation

## Slide 9: Differences in the Microcontrollers
Many Microcontrollers have no EEPROM
We need to secure critical system data
Flash ROM is programmed and erased block by block
  Block size is 8, 16, 32, or 64 bytes
This is not the case with EEPROM which is byte by byte programmable and eraseable.

## Slide 10: HCS912DP512 SFR Addresses

## Slide 11: Memory Address Verification Example
Verify the memory address for the following sections
  Registers 1 KB starting 000 hex
  Ram 12 KB starting 1000 hex
  Flash Rom 32 KB starting 8000 hex
Solution
  Register 1024 converts to 400 hex <= 0000 to 3FF
  Ram 12,288 converts to 3000 hex <= starting address is 1000 hex implies 1000 to 3FFF
  Flash Rom 32 KB converts to 8000 hex <= starting location 8000 hex implies 8000 to FFFF

## Slide 12: Dividing Memory Space into 4 Equal Sections
Range is 64 KB divided by 4 will result in 4 equal 16 KB sections
  3FFF is 16 KB
  Division 1 0000 to 3FFF for Registers, RAM and EEPROM
  Division 2 4000 to 7FFF for Fixed Code ROM
  Division 3 8000 to BFFF for page window
  Division 4 C000 to FFFF for Fixed Code ROM

## Slide 13: Accessing Memory Beyond 64 K
One of the most important registers in the microcontroller is the program counter (PC)
  This is incremented each time the CPU fetches an instruction from the program ROM
  The PC is 16 bits wide, meaning that only 64 K or 2^16 may be accessed.
  The result is that we will need to used page swapping to access memory beyond 64 K.

## Slide 14: Where the HCS12 Wakes up when it is Powered up
In the HCS12 family this is $FFFE
Power up is accomplished by applying required Vcc or activating Reset Pin
This means that the address of the first instruction must be stored at $FFFE
Locations $FFFE and $FFFF belong to the interrupt vector.
In some trainers the interrupt vector table is redirected to prevent users from overwriting the bootloader address

## Slide 15: MC9S12Dx512 Memory Allocation Using Page Window

## Slide 16: Single Chip and Expanded Modes in the HCS12
HCS12 can work in several modes
  Most widely used are single chip and expanded
  In single chip mode, all on chip memories are visible to the programmer and their addresses are set to fixed locations upon reset.
  In expanded mode one may connect to external memories of RAM and ROM and remap the on chip memories to different address locations
  In some development boards the HCS12 uses the external RAM for code development to avoid obsolescence of the Flash ROM

## Slide 17: Single Chip vs Expanded Mode in HCS12