## Slide 1: Section 2-3
HCS12 Addressing Modes

## Slide 2: HCS12 Addressing Modes
HCS12 has 6 distinct addressing modes
  Inherent
  Immediate
  Extended
  Direct
  Relative
  Indexed

## Slide 3: Inherent /Register Mode
This mode of addressing either involves no operand or it uses a register to hold the operand.
Examples
  NOP ; No Operation, waste a clock cycle
  STOP ; Stop the program counter
  ABA ; Add the contents of B to contents of A
  CLRA ; Clear register A
  INCB ; Increment register B
  INX ; Increment register X

## Slide 4: Immediate Addressing
In this mode the source operand is a constant which follows immediately behind the opcode, it must be preceded with a # sign. It may be used to load data into any of the registers
Examples
  LDAA #$25 ; load 25 hex into A
  LDAB #6C ; load 62 decimal into B
  LDD #$9FF2 ; load 9FF2 hex into D
  LDS #$7FF ; load 7FF hex into the stack pointer
  LDX #$559D ; load 559D hex into X

## Slide 5: More About Immediate Addressing
Because Register D is 16 bit and can be split into two 8 bit registers, namely A and B…
  LDD #$2550 ; load 2550 hex into D produces the same result as
    LDAB #$50 ; load 50 hex into B
    LDAA #$25 ; load 25 hex into A
      Note that A contains the more significant 8 bits
  LDD #$68975 ; load 68975 hex into D
    Produces an error because this value is larger than that which can be represented by 16 bits

## Slide 6: Extended Addressing
In this mode the Data is in RAM locations with a known address. We do not use the # sign in extended addressing
Examples
  LDAA $800 ; load value at location 800 hex into A
  LDAB $801 ; load value at location 801 hex into B

## Slide 7: STAA instruction
Moves the source to a memory location
  Example
    LDAA #$99 ; value of A becomes 99 hex
    STAA $800 ; value of address 800 hex becomes 99 hex
    STAA $801 ; value of address 801 hex becomes 99 hex
    STAA $802 ; value of address 802 hex becomes 99 hex
    STAA $803 ; value of address 803 hex becomes 99 hex
    STAA $804 ; value of address 804 hex becomes 99 hex

## Slide 8: Another STAA Example
Note the below section of code..
    LDAA #$33 ; value of A becomes 33 hex
    STAA $1200 ; location 1200 hex becomes 33 hex
    STAA $1201 ; location 1201 hex becomes 33 hex
    STAA $1202 ; location 1202 hex becomes 33 hex
    CLRA ; value of A becomes 00
    ADDA $1200 ; value of A becomes 33 hex
    ADDA $1201 ; value of A becomes 66 hex
    ADDA $1202 ; value of A becomes 99 hex
    STAA $1204 ; stores result into location 1204 hex

## Slide 9: YAE (yet another example)
Review the below section of code and provide relevant memory location contents
      LDAA #$99
      STAA $821
      LDAA #$85
      STAA $813
      LDAA #$3F
      STAA $814
      LDAA #$63
      STAA $815
      LDAA #$12
      STAA $816
Memory Map
Address | Data
0812 | 99
0813 | 85
0814 | 3F
0815 | 63
0816 | 12

## Slide 10: Little end vs Big end
From a story in “Gullivers Travels” about which end of an egg to open.
Freescale Microprocessors use the Big end convention
  Consider the sixteen bit register X
    LDX #$95F3 ; loads 95F3 hex into X
    STX $525 ; stores contents of X into location 525 hex
    High byte goes into lower location
    Now location 525 hex is 95 hex and location 526 hex is F3

## Slide 11: Big end convention example
Assume this memory map..
    Location 826 hex => $48
    Location 827 hex => $22
Upon instruction LDD $826
    High address is 827 hex
    Low address is 826 hex
    Register A subdivision of D contains $48
    Register B subdivision of D contains $22

## Slide 12: YAE of Big End
Consider the below code
    LDY #$9245
    STY $804
What will be stored at addresses 804 hex and 805 hex?
    According to big end, 804 hex stores high byte, and 805 hex stores low byte
    Value at 804 hex therefore is 92 hex
    And value at 805 hex is 45 hex

## Slide 13: Direct Addressing
This is a special case of extended addressing where the RAM address is only 8 bit
  Limits addresses from 00 to FF hex
  Since the special function registers (SFR) are located in this range we can use this method to access them
  These registers may be accessed by their names (easier) or their addresses (harder).
  PORTA has address 00 and PORTB has address 01

## Slide 14: Direct Addressing Examples
Note the below equivalent methods of storing contents of register A into PORTA
    STAA $00
    STAA PORTA
Note the below code which loads PORTA and PORTB with the value of 55 hex
    LDAA #$55
    STAA PORTA
    STAA PORTB

## Slide 15: Relative addressing
This is used exclusively by branch (jump) instructions
The address of the target location is relative to the current value of the PC
This is covered in more detail in Chapter 3 of the text

## Slide 16: Indexed Addressing
Index Registers X and Y as well as a displacement value are use to calculate the “effective” address (EA) of the operand data
We can use this mode to access both RAM and ROM data
Since X and Y are 16 bit we can access the entire 64 KB memory space
We can also add a fixed off-set value to the X or Y pointer

## Slide 17: Indexed Addressing Example
Note the below code segment..
    LDX #$800 ; 800 hex is loaded into register X
    LDAA #$55 ; 55 hex is loaded into register A
    STAA 0,X ; 55 hex is loaded into location 800 hex
    STAA 1,X ; 55 hex is loaded into location 801 hex
    STAA 2,X ; 55 hex is loaded into location 802 hex
    STAA 3,X ; 55 hex is loaded into location 803 hex

## Slide 18: Another Version of the Previous Example
    LDX #$800 ; load value of 800 hex into register X
    LDAA #$55 ; load value 55 hex into register A
    STAA 0,X ; load value 55 hex into location 800 hex
    INX ; increment X to 801 hex
    STAA 0,X ; load value 55 hex into location 801 hex
    INX ; Value of X becomes 802
    STAA 0,X ; load value 55 hex into location 802 hex
    INX ; increment X to value of 803 hex
    STAA 0,X ; load value 55 hex to location 803 hex
    One should now see how this could be done more efficiently in a loop

## Slide 19: Load and Store Instructions
Instruction | Operation
LDAA | Load A
LDAB | Load B
ADD | Load D
LDS | Load SP
LDX | Load X
LDY | Load Y
STAA | Store A
STAB | Store B
STD | Store D
STS | Store SP
STX | Store X
STY | Store Y

## Slide 20: Instruction Size of the HCS12
Size ranges from 1 to 5 bytes of machine code
Note the below:
  ABA ; 1 byte
  LDAA #$25 ; 2 byte
  LDAA $750 ; 3 byte
  LDD #$29F2 ; 3 byte

## Slide 21: LDAA
“LDAA #imm_val” instruction formation
Where, 0 ltoe i ltoe FF
Opcode | Opcode | Value | Value
1000 | 0110 | iiii | iiii

## Slide 22: LDDA
“LDAA ram_locl” instruction formation
Where 0 ltoe hhll ltoe FFFF
Opcode | Opcode | Location | Location | Location | Location
1011 | 0110 | h | h | l | l

## Slide 23: STAA
“STAA ram_loc” instruction formation
Where 0 ltoe hhll ltoe FFFF
Opcode | Opcode | Location | Location | Location | Location
0111 | 1010 | H | H | L | L