## Slide 1: Section 2.4
HCS12 Condition Code Register

## Slide 2
This is an 8 bit Register
Referred to as the flag register
Five of the flags are conditional flags
  C denoting carry
  H denoting half carry
  Z denoting zero
  N denoting negative
  V denoting overflow
Two of the flags, I and X, are used for interrupt masking
One of the flags, S, is used for the stop option

## Slide 3: C, the carry flag
Set whenever there is a carry out from the D7 bit
Affected after 8 or 16 bit addition or subtraction

## Slide 4: H, the half byte carry flag
Set when there is carry from D3 bit
Cleared otherwise
Used by operations that perform binary coded decimal arithmetic
Sometimes called the Auxiliary Carry or AC flag

## Slide 5: Z, the zero flag
Reflects the result of an arithmetic or logic operation
Set to 1 for a 0 result
Set to 0 if result is not zero
Useful for looping

## Slide 6: V, the overflow flag
This flag is set whenever the result of a signed number operation is too large
The sign bit will therefore be overwritten

## Slide 7: N, the negative flag
Bit D7, the MSB in binary representation of 8 bit signed numbers is used to represent sign
  It is 0 for positive numbers and 1 for negative numbers
N is 0 when D7 is 0
N is 1 when D7 is 1

## Slide 8: Map of the CCR register
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
S | X | H | I | N | Z | V | C
C Carry Flag
V Overflow Flag
Z Zero Flag
N Negative Flag
I Interrupt mask Bit
H Half Byte Carry Flag
X Interrupt Mask Bit
S Stop Bit

## Slide 9: Add Instructions and the CCR
What is the status of C, H, N, and Z after these instructions?
  LDAA #$38 ; Binary is 0011 1000
  ADDA #$2F ; Adding Binary 0010 1111
  Result 0110 0111 or 67 hex
  C bit is 0 because no carry beyond D7 bit
  H bit is 1 because there was carry from D3 bit
  N bit is 0 because D7 is 0
  Z bit is 0 because result was not 0

## Slide 10: Another ADD and CCR Example
Show the status of C, H, N, and Z flags after:
  LDAA #$9C ; Load 1001 1100 into accumulator
  ADDA #$64 ; Add 0110 0100 and keep result
  Result is 0000 0000 or 100 hex
  C bit is 1 because of carry from D7
  H bit is 1 because of carry from D3
  N bit is 0 because D7 is 0
  Z bit is 1 because the accumulator has all 0’s

## Slide 11: Yet Another ADD and CCR Example
Show the status of C, H, N, and Z flags after:
  LDDA #$88 ; load binary 1000 1000 into A
  ADDA #$73 ; add binary 0111 0011 and keep in A
  Result is 1111 1011 or FB hex
  C is 0, no carry beyond D7
  H is 0, no carry from D3
  N is 1, D7 is 1
  Z is 0, accumulator is not 0

## Slide 12: Not all instructions affect CCR
Insruction | H | N | Z | V | C
ABA | X | X | X | X | X
ADDA | X | X | X | X | X
ADDB | X | X | X | X | X
ANDA |  |  | X | X | 0
CLRA |  | 0 | 1 | 0 | 0
COMA |  | 1 | X | 0 | X
DAA |  | X | X | ? | X
DECA |  | X | X | X | 
INCA |  | X | X | X | 
ORAB |  | X | X | X | 
XGDX |  |  |  |  | 
X may be 0 or 1, blank means not affecting, ? means unknown

## Slide 13: Flag Bits and Decision Making
Instruction | Action
BCS | Branch if C = 1
BCC | Branch if C = 0
BEQ | Branch if Z = 1
BNE | Branch if Z = 0
BMI | Branch if N = 1
BPL | Branch if N = 0
BVS | Branch if V = 1
BVC | Branch if V = 0