## Slide 1: Section 2.5
HCS12 Data Format and Directives

## Slide 2: Data Format Representation
4 ways to represent a byte of data in the HCS12 assembler
  Hex
  Binary
  Decimal
  ASCII

## Slide 3: hex
Assembly:
  Precede number with $ sign
  Eg. LDDA #$25
C language
  Precede number with 0x
  Eg. PORTB = 0x99

## Slide 4: Binary Numbers
Number is preceded by % sign
  Eg. LDDA #% 00100101 ; 25 hex

## Slide 5: Decimal Number
There is no symbol in front of the number
  Eg LDDA #12 ; 0C hex

## Slide 6: ASCII CHARACTER
Single quotes around the character are used to denote it as ASCII.
  Eg. LDAA #’9’ loads the value for the character 9 (39 hex)
Double quotes are used for a string
  Use with the DC (define constant) directive

## Slide 7: Assembler Directives
These instructions give directions to the assembler as opposed to the CPU
  LDDA
    CPU
  EQU, ORG, END
    Assembler

## Slide 8: EQU
This is used to define a constant value or fixed address
  Eg. COUNT EQU $25 ; Value of Count defined as 25 hex
  LDDA #COUNT ; Value of register A is 25 hex

## Slide 9: SET
Same as EQU except that:
  Value assigned by the SET directive may be reassigned later

## Slide 10: Using EQU for fixed data assignment
DATA1 EQU $39 ; 8 BIT HEX DATA
DATA2 EQU $96F2 ; 16 BIT HEX DATA
DATA3 EQU % 00110101 ;BINARY 35 H
DATA4 EQU % 11110111 ;BINARY F7 H
DATA5 EQU % 1001011110001000; 9788 H
DATA6 EQU 28 ;DECIMAL 1C H
DATA7 EQU 2500 ;DECIMAL 16 BIT
DATA8 EQU ‘2’ :ASCII
DATA9 EQU ‘F’ ;ASCII

## Slide 11: USING EQU for RAM address assignment
MYCOUNT EQU 5
MYREG EQU $1200
  LDDA #MYCOUNT
  STAA MYREG ; NOW LOCATION 12OO H IS VALUE 5

## Slide 12: Another address example
MYVAL EQU $33
MYRAM EQU $1200 ;RAM ADRESS 1200 H
LDAA #MYVAL ;A = 33H
STAA MYRAM ; STORE A CONTENTS TO 1200 H
STAA MYRAM +1 ; A CONTENT TO 1201 H
STAA MYRAM +2 ; ACONTET TO 1202 H
CLR A ; CLEAR CONTENTS 0F A
ADDA MYRAM ; A=33 H
ADDA MYRAM +1 ; A=66H
ADDA MYRAM =2 ; A=99 H

## Slide 13: EXAMPLE putting 99 h into multiple locations
VAL_1 EQU $99 ; VAL_1 = 99 H
STAA MYBUF EQU $800;RAM ADDRESS 800 H
STAA MYBUF +1 ; RAM ADDRESS 801 H
STAA MUBUF +2 ; RAM ADDRESS 802 H
STAA MYBUF +3 ; RAM ADDRESS 803 H
STAA MYBUF +4 ; RAM ADDRESS 804 H

## Slide 14: ORIGIN DIRECTIVE
ORG indicates the beginning of the address space

## Slide 15: END DIRECTIVE
END indicates the end of the source source code.

## Slide 16: FCB Directive
FCB is used to define byte size variables
Can Also use DC.B
  ORG $850
  MYDAT1 DC.B
  ORG $860
  MYDAT2 FCB $33,,$66,$CC

## Slide 17: Form Constant Character Directive
Used to form ASCII strings
  ORG $8550
  MYMESS FCC “Hello World”

## Slide 18: Define Constant Byte Directive
DC.B allocates a byte sized variable for read only
  ORG $1000
  MYVALUE DC.B 5 ; MYVALUE = 5

## Slide 19: Define Constant Word Directive
DC.W defines word sized value for read only
  ORG $1000
  MYWORD DC.W $200 ; MYWORD = 200 H

## Slide 20: Define Space Byte Directive
DS.B
  ORG $1000
  MYARRAY DS.B 5 ; Sets aside 5 RAM bytes
  COUNTER DS.B 1 ; Set aside location for counter

## Slide 21: Define Space Word Directive
DC.W used to reserve a number of words in RAM
  ORG $1000
  MYARRAY DS.W 5 ; Sets aside 10 bytes or 5 words
  COUNTER DS.W 1 ;Sets aside location for16 bit counter

## Slide 22: Rules for Labels
Must be unique
Upper and Lower Case letters
Digits 0 – 9
Special Characters ?, ., @, _, $
Cannot use command names
Assembler will have a list of reserved labels