## Slide 1: SECTION 2.7
Assembling and Linking an HCS12 Program

## Slide 2: Steps Involved
Use a text editor to type in the Program
  In the case of HC12 microntrollers,
    Many are freely available with
      Text editor
      Assembler
      Linker
      Much more
    Code Warrior
.asm source file loaded into assembler
  Creates .o object file and .lst file
Then one or more .o files and assembles hex file and map
  The .s19 file is ready to be loaded into program ROM
Many Windiows based IDE assemblers combine steps 2 and 3

## Slide 3: You are dying to know more..
The .asm file is AKA the source file
The assemble converts .asm file to machine language creating the .o object file.
In Modular Programming (best practice), the linker links many programs together to generate a ready to burn hex file
Before linking we must verify error free code
  May use list file
  May use debugger

## Slide 4: Assembly Language Program Example
; ASSEMBLY LANGUAGE PROGRAM TO ADD SOME DATA
;STORE SUM IN RAM LOCATION 210 HEX
SUM EQU $210 ;RAM LOCATION 210 HEX FOR SUM
ORG $8000 ; START AT ADDRESS 8000 HEX
LDAA #$25 ; A = 25 HEX
ADDA #$34 ; ADD 34 HEX TO A, A=59 HEX
ADDA #$11 ;ADD 11 HEX TO A, A=6A HEX
ADDA #18 ;ADD 18 DECIMAL TO A, A = 7CH
ADDA #%00011100 ; A = 7C HEX + 1C HEX = 98 HEX
STAA SUM ; 98 HEX IS STORED AT LOCATION 210 HEX
HERE JUM HERE ; STAY HERE
END ;END OF SOURCE FILE

## Slide 5: LIST FILE FOR PREVIOUS PROGRAM
; ASSEMBLY LANGUAGE PROGRAM TO ADD SOME DATA
;STORE SUM IN RAM LOCATION 210 HEX
0210 SUM EQU $210 ;SUM ASSIGNED ADDRESS 210 HEX
8000 ORG $8000 ; START AT ADDRESS 8000H
8000 86 25 LDAA #$25 ; A = 25 HEX
8002 8B 34 ADDA #$34 ; A = 59 HEX
8004 8B 11 ADDA #$11 ; A = 6A HEX
8006 8B 12 ADDA #18 ; A = 7CH
8008 8B 1C ADDA #%00011100 ; A = 98 HEX
800A 7A 02 10 STAA SUM ; 98 HEX IS STORED IN LOCATION 210
800D 06 80 0D HERE JUMP HERE ; STAY HERE
END

## Slide 6: Machine Code for Previous Program
ROM ADDRESS | MACHINE LANGUAGE | ASSEMBLY LANGUAGE
8000 | 8625 | LDAA #$25
8002 | 8B34 | ADDA #$34
8004 | 8B11 | ADDA #$11
8006 | 8B12 | ADDA #18
8008 | 8B1C | ADDA #%00011100
800B | 7A021 | STAA SUM
800D | 06800D | HERE STAY HERE

## Slide 7: ROM Contents for previous program
Address | Code | Address | Code
8000 | 86 | 8009 | 1C
8001 | 25 | 800A | 7A
8002 | 8B | 800B | 02
8003 | 34 | 800C | 10
8004 | 8B | 800D | 06
8005 | 11 | 800E | 80
8006 | 8B | 800F | 0D
8007 | 12 |  | 
8008 | 8B |  | 

## Slide 8: Executing a Program Byte by Byte
Assume the above program has been linked and downloaded.
  PC is set to location $8000
    Opcode 86 is fetched from the location
    Next byte contains the data $25
    PC incremented to $8002 and Opcode $8B is fetched
    Next byte contains the data $34
    PC incremented to $8004, Opcode $8B fetched with data $11
    PC incremented to $8006, Opcode 8B, Data $12
    PC incremented to $8008, Opcode 8b, Data $1C
    PC incremented to $800A, Opcode 7A, Data $0210
    PC incremented to $800D, Opcode 06, Data $800D