## Slide 1: SECTION 2.8
Stack and Data Transfer Instructions

## Slide 2: How Stacks are Accessed in the HCS12
Stack is a Section of RAM
  We must have a register to point to it.
  The 16 bit wide SP is used for this
  SP can receive $0000 to $FFFF
  Storing CPU register is called a PUSH
  Retrieving from SP is called a PULL

## Slide 3: Pushing onto the Stack
Stack Pointer points to last used location of the stack
  SP is decremented each time we push
  This is a common convention

## Slide 4: Push example
Show the stack and stack pointer for the following code segment:
LDS #$1200 ;SP = $1200
LDY #$F395 ;Y = $F395
LDAA #$25 ;A = $25
LDAB #$12 ;B = $12
PSHA ; PUSH A ONTO STACK
PSHB ;PUSH B ONTO STACK
PSHY ; PUSH Y ONTO STACK
START | AFTER PSHA | AFTER PSHB | AFTER PSHY
11FC - | 11FC - | 11FC - | 11FC – F3
11FD - | 11FD - | 11FD - | 11FD – 95
11FE - | 11FE - | 11FE - 12 | 11FE - 12
11FF - | 11FF - 25 | 11FF - 25 | 11FF - 25
SP - 1200 | SP – 11FF | SP – 11FE | SP – 11FC

## Slide 5: Pulling From the Stack
This is pulling the contents of the stack back into a register
  Opposite of pushing
  Top Byte of the stack is pulled to a particular register
  Stack pointer is incremented on a pull

## Slide 6: Stack and Scratch Pad Conflict
SP points to last used location of the stack
  Push decrements SP
    The reason for this is to make sure that SP is growing toward beginning of RAM address
    Assures that we will not reach the last location of RAM address
    Programmer is responsible to set the initial SP to last RAM address before stacks are used
  Pull increments SP

## Slide 7: Pull example
Assume initial values for starting SP address 12FC
12FC 54
12FD F9
12FE 76
12FF 6C
What are contents of register and SP after below code?
PULA ;PULL STACK INTO A
PULB ;PULL STACK INTO B
PULX ;PULL STACK INTO 16 BIT REGISTER X
Start | After PULA | After PULB | After PULX
12FC - 54 |  |  | 
12FD – F9 | 12 FD – F9 |  | 
12FE – 76 | 12FE - 76 | 12FE – 76 | 
12FF – 6C | 12FF – 6C | 12FF – 6C | 
SP = 12FC | SP = 12FD A = 54 | SP = 12FE B = F9 | SP = 1300 X = 766C

## Slide 8: MC9S12DP512 Stack
D7 STACK D0
STACK
$800 BEGINNING OF RAM
$3FFF END OF RAM
Stack Pointer is
Decremented as
Data Pushed onto
Stack
Stack Pointer is
Incremented as
Data Pulled from Stack
Top of Stack
First Available
Memory Location

## Slide 9: Another Stack and Stack Pointer Example
Show the Stack and Stack Pointer for below code
LDS #$4000
LDAA #$25
LDAB #$12
ABA ; ADD ACUMULATOR A AND B RESULT IN A
PSHA
PSHB
ABA
PSHA
START | AFTER PSHA | AFTER PSHB | AFTER PSHA
3FFC | 3FFC | 3FFC | 3FFC
3FFD | 3FFD | 3FFD | 3FFD -49
3FFE | 3FFE | 3FFE - 12 | 3FFE - 12
3FFF | 3FFF - 37 | 3FFF - 37 | 3FFF - 37
SP = 4000 | SP = 3FFF | SP = 3FFE | SP = 3FFD

## Slide 10: Stack Instructions
Instruction | Operation
PSHA | PUSH A
PSHB | PUSH B
PSHC | PUSH C
PSHD | PUSH D
PSHX | PUSH X
PSHY | PUSH Y
PULA | PULL A
PULB | PULL B
PULC | PULL C
PULD | PULL SP
PULX | PULL X
PULY | PULL Y

## Slide 11: Data Transfer Instructions
INSTRUCTION | OPERATION
TAB | TRANSFER A TO B
TBA | TRANSFER B TO A
TAP | TRANSFER A TO CCR
TPA | TRANSFER CCR TO A
TSX | TRANSFER SP TO X
TXS | TRANSFER X TO SP
TSY | TRANSFER SP TO Y
TYS | TRANSFER Y TO SP
TFR | TRANSFER REGISTER TO REGISTER
EGDX | EXCHANGE D WITH X
EGDY | EXCHANGE D WITH Y
EXG | EXCHANGE REGISTER WITH REGISTER
MOVB | MOVE BYTE FROM SOURCE TO DEST
MOVW | MOVE WORD FROM SOURCE TO DEST

## Slide 12: ERATTA
Assuming we are proficient in assembly language for other processors such as 8051
  Ram area can be thought of as a large number of register
  We can rename them as long as we do not use reserved names for SFR’s
We will be working with Code Warrior soon
  Allows us to view register contents
  Allows single step debugging