## Slide 1: Section 3.2
JSR and CALL Instructions

## Slide 2: JSR – Jump to Subroutine
3 byte instruction
  First byte is opcode
  Bytes 2 and 3
  Address range is 0000 – FFFF H
  The address of instruction below jump is saved to stack
  Upon subroutine fetch, PC of next instruction saved to stack and control passes to subroutine
  RTS returns control to calling program

## Slide 3
; This program toggles all of the bits of Port B by sending 55 H and AA H repeatedly
; A time delay is provided between each data write
INCLUDE ‘nc9s12dp512.inc’
MYREG EQU $8O8 ; LOCATION 808 STORES COUNTER
ORG $8000 ; STARTING ADDRESS
LDS #$4000 ;INITIALYZE STACK POINTER
BACK LDAA #$55 ; A = 55 H
STAA PORTB ; SEND 55H TO PORTB
JSR DELAY ; JUMP TO DELAY SUBROUTINE
LDAA #$AA ; A = AA H
STAA PORTB ; SEND AA H TO PORTB
JSR DELAY ; JUMP TO DELAY SUBROUTINE
BRA BACK ; INFINITE LOOP
; Time Delay Subroutine
ORG $8300 ; PUT TIME DELAY AT ADDRESS 8300 H
DELAY LDAA #$FF ; A = 255 D
STAA MYREG ; MYREG = FF H
AGAIN NOP
NOP ; 2 CLOCK CYCLES ARE WASTED
DEC MYREG ; DECREMENT COUNTER
BNE AGAIN ; LOOP UNTIL COUNTER IS 0
RTS ; RETURN TO CALLER
END ; END OF ASM FILE

## Slide 4: JSR Instruction and Role of Stack
Stack saves address below JSR instruction
  RTS will return to the instruction below the JSR instruction
  Upon executing the first JSR, address of LDAA #$AA is pushed onto the stack and instructions starting at 8300 H commence
  The counter is set to 255 D within the DELAY subroutine which is therefore executed 255 times
  When counter equals 0 control is transferred to RTS instruction
  Actual time delay dependent on clock rate

## Slide 5: List file for previous program

## Slide 6: Memory Map and SP Before and After JSR
Address | Before First JSR | After First JSR | After RTS | After Second JSR | After RTS
3FFC |  |  |  |  | 
3FFD |  |  |  |  | 
3FFE |  | 80 |  | 80 | 
3FFF |  | 0A |  | 11 | 
SP VALUE | 4000 | 3FFE | 4000 | 3FFE | 4000

## Slide 7: Using Complement A to do the same thing as previous example

## Slide 8: Stack Usage and its Lower Limit
Stack is most often used for Calls and Interrupts.
  Stack keeps track of where CPU should return after completing subroutine
  Be careful about manipulating Stack Contents
  Could cause unexpected results
  Also make sure stack does not reach lowest address
    This can happen if we have too many nested calls

## Slide 9: Calling Many Subroutines from Main
It is common and good practice to call subroutines from the main program
  Allows development and debug at subroutine level
  Allows development of subroutine by different programmer
    This reduces the code development interval

## Slide 10: Another List Example

## Slide 11: Call
On chip ROM on HCS12 can exceed 512 Kbyte
  Use of CALL will allow access out of 64 KB space
  Accessing Flash ROM outside of 64 KB address range requires use of PPAGE register
  Call is a 4 Byte Instruction
  Target address of subroutine may be within 512 Kbytes of CALL
  One byte of command is for PPAGE value
  Call uses 3 bytes of stack
  Use RTC to return from CALL

## Slide 12: Calling Many Subroutines
; Main Program Calling Subroutines
INCLUDE ‘mc9s12dp512.inc’
ORG $8000
LDS #$4000 ; Initialize Stack Pointer
; Other Instructions may be here
MAIN JSR SUBR1
; Other Instructions may be here
JSR SUBR2
JSR SUBR3
HERE BRA HERE ; Stay here
; End of Main
SUBR1 ; Some code
RTS
SUBR2 ; Some code
RTS
SUBR3 ; Some code
RTS
END ;End of asm file

## Slide 13: CALL vs. JSR
Assume your particular HCS12 is equipped with 32K on chip Flash ROM.
  Which command would you use?
  JSR is 3 byte instruction and saves ROM
  We do not need to use CALL because we will not go out of 64 KB range

## Slide 14: Delay Calculation for HCS12
Two factors affect accuracy of delay
  Crystal Frequency
    Connected to XTAL AND EXTAL pins
  Internal Design of the HCS12
    Three ways to reduce number of clock cycles per instruction
      Harvard Architecture
      RISC Architecture
      Pipelining – Used extensively in HCS12 due to backward compatibility reasons

## Slide 15: HCS12 Call Instruction Summary
Instruction | Action | Instruction Size
JSR | Branch to an address within 64 Kbytes | 3 byte
BSR | Branch to an address within 256 Kbytes | 2 byte
RTS | Return from subroutine, used with JSR and BSR | 1 byte
CALL | Call an address beyond 64 Kbyte | 4 byte
RTC | Return from subroutine in expanded memory, used with CALL | 1 byte

## Slide 16: Pipelining
The idea of pipelining is to allow CPU to fetch and execute at the same time.

## Slide 17: Instruction Queue and Branch Penalty
Pipelining is widely used in today’s HCS12
  Relies on a buffer to hold pre-fetched instructions
  The buffer will be cleared on a branch or call instruction
  The CPU needs to the new instructions are fetched from the subroutine
  This is called a branch penalty
  Number of clock cycles in condition branch depends on status bit
    No branch, 1 clock cycle
    Branch, 3 clock cycles
  On another note, differing addressing modes may take different clock cycles for the same command

## Slide 18: ADDA Instruction Cycle Times in HCS12/9S12 Datasheet
Addressing Mode | Access Detail | Clock Cycles
Immediate | P | 1
Direct | rPf | 3
Extended | rPo | 3
Indexed no Offset | rPf | 3
Indexed 1 – 9 bit signed offset | rPo | 3
Indexed 2 – 16 bit singned offset | frPP | 4
Indexed Indirect 2 | fIfrPf | 6
Indexed D | fIPrPf | 6
Notes: I

## Slide 19: Access Description
f – free cycle CPU does not use bus
r – read indirect pointer
P – program word fetch, always an aligned word
o – optional program word fetch
l – read indirect pointer

## Slide 20: How to estimate delay loop interval
; Estimate the length of a delay loop for a crystal frequency of 5 MHz
MYREG EQU #$1208 ; USE LOCATION 1208 AS COUNTER
DELAY LDAA #200 ; 1 CLOCK CYCLE
STAA MYREG ; 3 CLOCK CYCLE
AGAIN NOP ; 1 CLOCK CYCLE
NOP ; 1 CLOCK CYCLE
DEC MYREG ; 4 CLOCK CYCLE
BNE AGAIN ; 3 CLOCK CYCLE
; HCS12 USES ½ OF OSCILLATOR FREQUENCY FOR CPU INSTRUCTION TIME OR 2.5 MHz
; TIME IS INVERSE OF FREQUENCY OR 0.4 MICROSECONDS
; THE AGAIN LOOP USES 9 CYCLES PER LOOP FOR 200 LOOPS
; TOTAL TIME IS 200 X 9 X 0.4 OR 720 MICROSECONDS

## Slide 21: Bottom Line
Use timers for more accurate software generated delays
This is covered in detail in Chapter 9