## Slide 1: Section 3.3
Programs Using Indexed Addressing Mode

## Slide 2: Clearing the RAM buffer
; How to clear the RAM locations using indexed addressing mode
LDX #$800 ; LOADS 800 H INTO REG X
CLRA ; A = 0
STAA 0,X ; CLEARS LOCATION 800 H
INX ; INCREMENTS X TO 801 H
STAA 0,X ; CLEARS LOCATION 801 H
INX ; INCREMENTS X TO 802 H
STAA 0,X ; CLEARS LOCATION 802 H
INX ; INCREMENTS X TO 803 H
STAA 0,X ; CLEARS LOCATION 803 H
; HOW COULD WE DO THIS WITH A LOOP?

## Slide 3: Clearing RAM Locations Using a Loop
R1 EQU $860 ; ADDRESS OF COUNTER
LDX #$800 ; SET POINTER X
LDAA #50 ; A = 50 D
STAA R1 ; SETS THE COUNTER TO 50 D
CLRA ; A = 0
OVER STAA 0,X ; CLEARS LOCATION 80n H n = 0 - 49
INX ; INCREMENT X TO 801 H
DEC R1 ; DECREMENT THE COUNTER
BNE OVER ; REPEAT IF R1 NE 0
; WE COULD PROABABLY DO THIS 2 BYTES AT A TIME…..

## Slide 4: Clearing Ram Locations with loop 2 bytes at once! Nothing but net
R1 EQU $860 ; LOCATION OF COUNTER VARIABLE IS 860 H
LDX #$800 ; SET POINTER X
LDAA #25 ; A = 25 D
STAA R1 ; COUNTER VALUE IS 25 D
CLRA ; A = 0
OVER STD 0,X ; LOCATION 80n and 80n + 1 cleared n = 0 to 48 even number
INX ; INCREMENT X
INX ; INCREMENT AGAIN
DEC R1 ; DECREMENT COUNTER
BNE OVER ; BRANCH TO OVER UNLESS R1 = 0

## Slide 5: Moving a Block of Data
; PROGRAM TO MOVE A BLOCK OF DATA FROM 900 H TO 1100 H
R1 EQU $810 ; SETS LOCATION OF COUNTER TO 810
LDX #$900 ; SETS VALUE OF POINTER X
LDY #$1100 ; SETS VALUE OF POINTER Y
LDAA #50 ; A = 50 D
STAA R1 ; VALUE OF COUNTER BECOMES 50 D
OVER LDAA 0,X ; LOAD BYTE POINTED TO BY X
STAA 0,Y ; STORE IN LOCATION POINTED TO BY Y
INX ; POINT TO NEXT SOURCE LOCATION
INY ; POINT TO NEXT TARGET LOCATION
DEC R1 ; DECREMENT COUNTER
BNE R1 ; LOOP UNTIL COUNTER IS 0
; COULD THIS BE CONSIDERED TO BE A COPY PROGRAM??

## Slide 6: Move / Copy Data 2 Bytes at a Time
; Program to move/copy two bytes at a time
R1 EQU $8IO ; LOCATION OF COUNTER VARIABLE
LDX #$900 ; STARTING LOCATION OF SOURCE
LDY #$1100 ; STARTING LOCATION OF DESTINATION
LDAA #25 ; A = 25 D
STAA R1 ; COUNT VARIABLE HAS VALUE OF 25 D
OVER LDD 0,X ; LOAD A WORD FROM LOCATION POINTED TO BY X
STD 0,Y ; STORE WORD INTO LOCATION POINTED TO BY Y
INX
INX ; INCREMENT X TO NEXT EVEN NUMBER
INY
INY ; INCREMENT Y TO NEXT EVEN NUMBER
DEC R1 ; DECREMENT COUNTER VALUE
BNE OVER ; LOOP UNTIL COUNTER = 0

## Slide 7: Using the MOV Command
Two move commands are available in HCS12 assembly language
  MOVB
    Moves byte
  MOVW
    Moves word
  Source Operand can be immediate or another memory location
  Note the following segment
; program to toggle Port B using MOVB
BACK MOVB #$55,PORTB ; MOVES 55 H TO PORTB
JSR DELAY ; JUMPS TO DELAY SUBROUTINE
MOVB #$AA ; MOVES AA H TO PORTB
JSR DELAY ; JUMPS TO DELAY SUBROUTINE
BRA BACK ; BRANCHES BACK TO BEGINNING

## Slide 8: MOVB Can Replace Combination of LDAA and STAA
; a previous example rewritten around MOVB
COUNT EQU $825 ; LOCATION OF COUNTER VARIABLE 825 H
MYRAM EQU $850 ; SUM STORED AT THIS LOCATION
MOVB #15,COUNT ; VALUE OF COUNT IS 15 D
CLRA ; A = 0
AGAIN ADDA #3 ; SUM ACCUMULATED IN A
DEC COUNT ; DECREMENT COUNTER
BNE AGAIN ; LOOP UNTIL COUNT = 0 THEN NEXT STEP
STAA MYRAM ; SUM STORED

## Slide 9: Moving a Block of Data Using MOVB
; moves block of data from 900 h to 1100 h
R1 EQU $810 ; LOCATION OF COUNTER
LDX #$900 ; POINTS TO FIRST SOURCE LOCATION
LDY #$1100 ; POINTS TO FIRST TARGET LOCATION
LDAA #50 ; A = 50 D
STAA R1 ; COUNTER VARIABLE BECOMES 50 D VALUE
OVER MOVB 0,X 0,Y ; MOVES A BYTE FROM SOURCE TO DESTINATION
INX ; INCREMENT TO NEXT SOURCE LOCATION
INY ; INCREMENT TO NEXT TARGET LOCATION
DEC R1 ; DECREMENT COUNTER
BNE AGAIN ; LOOP UNTIL R1 = 0 THEN NEXT STEP

## Slide 10: Moving a Block of Data Using MOVW
; moves a block of data a word at a time
R1 EQU $810 ; LOCATION OF COUNTER VARIABLE
LDX #$900 ; POINTS TO FIRST SOURCE LOCATION
LDY #$1100 ; POINTS TO FIRST DESTINATION LOCATION
LDAA #25 ; A = 25 D
STAA R1 ; VALUE OF COUNTER INITIALLY 25 D
OVER MOVW 0,X 0,Y ; MOVE FROM X LOCATION TO Y LOCATION
INX
INX ; X INCREMENTED BY 2
INY
INY ; Y INCREMENTED BY 2
DEC R1 ; DECREMENT COUNTER
BNE OVER ; LOOP UNTIL COUNTER = 0, THEN NEXT