## Slide 1: Section 4-2
I/O BIT MANIPULATION

## Slide 2: Bit addressability of I/O Ports
Some times it is convenient to access individual bits of Ports and RAM addresses
Instruction | Function
BSET mem, mask byte | Bit Set RAM location
BCLR mem, mask byte | Bit Clear RAM location
BRCLR | Branch if bit is clear
BRSET | Branch if bit is set

## Slide 3: BSET EXAMPLE
; A PROGRAM TO TURN ON LED CONNECTED TO PINS OF PORT B INCLUDING DELAY
LDAA #$FF ; A = FF D
STAA PORTB ; PORTB IS OUTPUT
BSET PORTB,%00000001 ; PB0 IS 1
JSR DELAY ; ZZZZ
BSET PORTB,%00000010 ; ONLY PB1 IS 1
JSR DELAY ; ZZZZ
BSET PORTB,%00000100 ; ONLY PB2 IS 1
JSR DELAY ; ZZZZ
BSET PORTB,$08 ; ONLY PB3 IS 1
JSR DELAY ; ZZZZ
BSET PORTB,$10 ; ONLY PB4 IS 1
JSR DELAY ; ZZZZ
BSET PORTB,$20 ; ONLY PB5 IS 1
JSR DELAY ; ZZZZ
BSET PORTB,$40 ; ONLY PB6 IS 1
JSR DELAY ; ZZZZ
BSET PORTB,$80 ; ONLY PB7 IS 1
JSR DELAY ; ZZZZ

## Slide 4: BCLR Example
; PROGRAM TO TOGGLE PB2 AND PB0
BSET DDRB,%00000101 ; THIS MAKES PB2 AN PB0 OUTPUT PINS
AGAIN BSET PORTB,%00000101 ; PB2 AND PB0 ARE HIGH
JSR DELAY ; ZZZZ
BCLR PORTB,%00000101 ; PB2 AND PB0 ARE LOW
JSR DELAY ; ZZZZ
BRA AGAIN ; INFINITE LOOP

## Slide 5: Example Program
; PROGRAM TO CREATE A 50% DUTY CYCLE SQUARE WAVE ON PORTA BIT 0
BSET DDRA,%00000001 ; BIT ZERO IS OUTPUT
HERE BSET PORTA,%00000001 ; PA0 IS HIGH
JSR DELAY ; ZZZZ
BCLR PORTA,%00000001 ; PA0 IS LOW
JSR DELAY ; ZZZZ
BRA HERE ; INFINITE LOOP

## Slide 6: Example Program
; PROGRAM TO CREATE A 66% DUTY CYCLE SQUARE WAVE ON BIT 4 OF PORT A
BSET DDRA,$04 ; DDRA BIT 4 IS OUTPUT
BACK BSET PORTA,$04 ; BIT 4 IS HIGH
JSR DELAY ; ONE RINGY DINGY
JSR DELAY ; TWO RINGY DINGIES
BCLR PORTA,$04 ; BIT 4 IS LOW
JSR DELAY ; ONE DELAY
BRA BACK ; INFINITE LOOP

## Slide 7: Example Program Segment
; PROGRAM TO MONITOR PB2 BIT UNTIL IS BECOMES HIGH THEN WRITE A VALUE TO
; PORT A THEN SEND A HIGH TO LOW PULSE TO PE3
BCLR DDRB,%0000100 ; PB2 IS INTPUT
LDAA #$FF ; VALUE OF A IS FF H
STAA DDRA ; A IS OUTPUT
LDAA #$45 ; VALUE OF A IS 45 H
AGAIN BRSET PORTB,%00000100,OVER ; BRANCH TO OVER IF PB2 IS HIGH
BRA AGAIN ; LOOP UNTIL, MYSTERIOUSLY, PB2
; IS LOW
OVER STAA PORTA ; WRITING 45 H TO PORT A
BSET PORTE,%00001000 ; PE3 IS HIGH
BCLR PORTE,%00001000 ; PE3 IS LOW

## Slide 8: Example Code Segment
; ANOTHER WAY TO ACCOMPLISH THE PREVIOUS EXAMPLE USING BRCLR
; INSTRUCTION
BCLR DDRB,%00000100 ; PB2 IS INPUT
LDAA #$FF ; A = FF H
STAA DDRA ; PORT A IS OUTPUT
BSET DDRE,%00001000 ; PE3 IS OUTPUT
LDAA #$45 ; A = 45 H
AGAIN BRCLR PORTB,%00000100,AGAIN ; CHECK IF PB2 IS LOW, IF SO BRANCH
; TO AGAIN
STAA PORTA ; ELSE WRITE PORT A
BSET PORTE,%00001000 ; PE3 IS HIGH
BCLR PORTE,%00001000 ; PE3 IS LOW

## Slide 9: Code Example Segment
; THINK ABOUT THE APPLICATION OF ALARM MONITORING. WE COULD USE PB3 AS
; THE BIT THAT MONITORS THIS CONDITION, AND FURTHER ASSUME THAT IT IS
; PULLED LOW WHEN THE DOOR IS OPEN, IT IS A REQUIREMENT TO SEND A HIGH TO
; LOW PULSE TO PE5 TO TURN ON A BUZZER
BCLR DDRB,%00001000 ; PB3 IS INPUT
BSET DDRE,%00100000 ; PE5 IS OUTPUT
HERE BRSET PORTB,%00001000,HERE ; BRANCH IF PB3 IS HIGH TO HERE
BSET PORTE,%00100000 ; PE5 IS HIGH
BCLR PORTE,%00100000 ; PE5 IS LOW

## Slide 10: Example Program Code Segment
; Program to monitor status of a switch and react accordingly by writing ASCII to Port A
BCLR DDRB,%00000100 ; PB2 IS INPUT
LDAA #$FF ; A = FF H
STAA DDRA ; PORT A IS OUTPUT
AGAIN BRSET PORTB,%00000100,OVER ; BRANCH IF PB2 IS HIGH TO OVER
LDAA #‘N’ ; A = ASCII N
STAA PORTA ; VALUE OF PORTA IS ASCII N
OVER LDAA #’Y’ ; A = ASCII Y
STAA PORTA ; VALUE OF PORTA IS ASCII Y
BRA AGAIN ; STAY ON THE HUNT

## Slide 11: Example Program Code Segment
; This program reads switch status and writes to a pin connected to an LED
BCLR DDRB,%00000001 ; PB0 IS INPUT
BSET DDRB,%10000000 ; PB7 IS OUTPUT
BACK BRSET PORTB,%00000001,OVER ; BRANCH TO OVER IF PB0 IS HIGH
BCLR PORTB,%10000000 ; SET PB7 LOW LED IS OFF
BRA BACK ; CHECK IT AGAIN
OVER BSET PORTB,%10000000 ; SET PB7 HIGH LED IS ON
BRA BACK ; CHECK IT AGAIN

## Slide 12: Are You Sick and Tired of Examples? Please be Patient for One More
; A program to monitor status of a switch and save the status in a particular RAM
; location
MYBYTE EQU $820 ; LOCATION FOR STATUS
BCLR DDRB,$00000001 ; PB0 IS INPUT
BACK BRSET PORTB,%00000001,OVER ; BRANCH TO OVER IF PB0 IS HIGH
BCLR MYBYTE,%00000001 ; MAKE BIT 0 LOW OF MYBYTE
BRA BACK ; CHECK IT AGAIN
OVER BSET MYBYTE,%00000001 ; BIT 0 OF MYBYTE IS HIGH
BRA BACK ; CHECK IT AGAIN