## Slide 1: Chapter 5
Arithmetic, Logic Instructions and Programs

## Slide 2: Learning Objectives
Upon completion, Students will be able to:
Define the range of numbers in HCS12 for unsigned data
Code addition and subtraction of numbers for unsigned numbers
Perform addition of BCD data
Code HCS12 multiplication a division of unsigned numbers
Code HCS12 logic instructions: AND, OR, and EX-OR
Code HCS12 assembly instructions for bit shift and rotate
Use HCS12 logic instructions for bit manipulation
Use Compare for program control
Code HCS12 rotate instructions and data serialization
Explain BCD system of data representation
Contrast and compare packed and unpacked BCD data
Code HCS12 programs for ASCII and BCD data conversion
Define the range of numbers possible in HCS12 for signed data

## Slide 3: Arithmetic Instructions and Programs
Unsigned number
  All bits used for data, none for sign
  Operand byte can be 00 to FF
One way to add is to use the A register
  ADDA Operand ; A = A + Operand
  Sum stored in A register
  Result could change C, H, Z, N, or, V bits of CCR

## Slide 4: CCR Example from ADDA Instruction
; Show how the flag register is affected by the following instructions
LDAA #$F5
ADDA #$B
; Solution in Hex
F5 + B = 100 ; A = 00
; Solution in Binary
1111 0101 + 0000 1011 = 0000 0000 ; A = 0000 0000
; C = 1 because of carry from Bit 7
; Z = 1 because A = 00 H
; H = 1 because of carry from Bit 3 to Bit 4

## Slide 5: Addition of individual bytes and words
ADDA addition of A register and individual bytes stored in RAM locations
  Recall that memory to memory location arithmetic is not allowed in HCS12 assembly language
  It can be important to check the carry flag after each operation
ADCA instruction (Add with carry to A)
  Used for adding 16 bit operands

## Slide 6: Using a Ram location to accumulate carry bits
; 4 Initialized RAM locations are added to store a sum according to Big Endian
; convention
L_BYTE EQU $807 ; RAM LOCATION LOW BYTE OF SUM
H_BYTE EQU $806 ; RAM LOCATION OF HIGH BYTE OF SUM
CLRA ; A = 0
STAA H_BYTE ; VALUE OF HIGH BYTE IS 0
ADDA $840 ; INITIAL VALUE OF LOC 840 ADDED TO A
BCC N_1 ; BRANCH TO N_1 LABLE IF NO CARRY INC H_BYTE ; ELSE INCREMENT H_BYTE
N_1 ADDA $841 ; INITIAL VALUE OF 841 ADDED TO A
BCC N_2 ; BRANCH TO N_2 IF NO CARRY
INC HBYTE ; ELSE INCREMENT H_BYTE
N_2 ADDA $842 ; ADD VALUE OF NEXT MEMORY LOCATION
BCC N_3 ; BRANCH TO N_3 IF NO CARRY
INC HBYTE ; ELSE INCREMENT H_BYTE
N_3 ADDA $843 ; ADD VALUE OF NEXT MEMORY LOCATION
BCC N_4 ; BRANCH TO N_4 IF NO CARRY
INC H_BYTE ; ELSE INCREMENT H_BYTE
N_4 STAA L_BYTE ; RESULT OF ADDITION STORED IN L_BYTE

## Slide 7: Once more by the numbers
Assume initial values of $840 thru $843 are 7D, EB, C5, and 5B respectively in hex
  Does it really matter about the respective part?
  1st addition, 7D + 0 = 7D no carry, branch to N_1
  2nd addition, 7D + EB = 168 C = 1 increment H_BYTE, A = 68, H_BYTE = 1
  3rd addition, 68 + C5 = 12D, C =1, increment H_BYTE, A = 2D, H_BYTE = 2
  4th addition, 2D + 5B = 88 C = 0, no carry, branch to N_4
  Wrap up, Store 88 to low byte, and high byte value is 02

## Slide 8: Some of you are thinking…..
Couldn’t this be a little more elegant?
LBYTE EQU $807 ; RAM LOCATION OF LOW BYTE OF SUM
HBYTE EQU $806 ; RAM LOCATION OF HIGH BYTE OF SUM
COUNT EQU $800 ; RAM LOCATION OF COUNT
LDDA #4 ; LOAD COUNTER VALUE INTO A
STAA COUNT ; INITIALYZE COUNTER VALUE
CLRA ; A = O
STAA HBYTE ; INITIALYZE HBYTE
LDX #$840 ; SET POINTER TO FIRST DATA ADDRESS
BACK ADDA 0,X ; ADDS VALUE AT ADDRESS TO A
BCC OVER ; BRANCH TO OVER IF NO CARRY
INC HBYTE ; ELSE INCREMENT HBYTE
OVER INX ; GETS NEXT ADDRESS
DEC COUNT ; COUNTER IS DECREMENTED
BNE BACK ; BRANCH IF COUNTER NE 0
STAA LBYTE ; STORE AFTER LOOPING COUNT TIMES

## Slide 9: Example using ADCA
; Program to add two 16 bit numbers using ADCA instruction. The numbers are 3CE7
; H and 3B8D H. Assume big endian convention, and 3B8D are stored in locations 807
; and 806. The result is stored in locations 808 and 809
LDAA #$E7 ; A = VALUE OF FIRST NUMBER LOW BYTE
ADDA $807 ; LOCATION OF NEXT LOW BYTE
; E7 + 8D = 174 AND C = 1
STAA $809 ; STORE ACCORDING TO CONVENTION
LDAA #$3C ; A = VALUE OF FIRST NUMBER HIGH BYTE
ADCA $806 ; A = A + VALUE OF NEXT HIGH BYTE + 1
STAA $808 ; STORE RESULTANT HIGH BYTE BIG ENDIAN

## Slide 10: Why doesn’t the fool use ADDD?
LDD #$3CE7 ; GET FIRST 16 BIT NUMBER
ADDD $806 ; GET SECOND 16 BIT NUMBER
STD $808 ; STORE BIG ENDIAN
Answer..
  In the general case we have multi-byte addition
  Consider two 4 byte numbers
    56F398C2 stored in 810 H thru 813 H
    2B45F387 stored in 850 h thru 853 H
  And, if you can, please contain your excitement to the next slide…

## Slide 11: Adding Multi-Byte Numbers
; Program to add two multi-byte numbers
MYCOUNT EQU $800 ; ADDRESS OF COUNTER VARIABLE
LDAA #4 ; A = 4 D
STAA MYCOUNT ; VALUE OF MYCOUNT IS 4 D
CLRA ; A = 0
LDX #$813 ; X POINTER
LDY #$853 ; Y POINTER
CLC ; CLEAR CARRY FLAG
BACK LDAA 0,X ; LOAD BYTE AT POINTED ADDRESS
ADCA 0,Y ; ADD BYTE AT POINTED ADDRESS
STAA 0,Y ; STORE WITH CARRY
DEX ; DECREMENT POINTER X
DEY ; DECREMENT POINTER Y
DEC MYCOUNT ; DECREMENT LOOP COUNTER
BNE BACK ; BRANCH IF COUNTER NE 0

## Slide 12: Binary Coded Decimal
In everyday life we use base 10
  Two basic types
    Packed
    Unpacked
    Unpacked BCD
      Lower 4 bits represent the number
      Upper 4 bits are 0
      Requires 8 bit register
    Packed BCD
      Uses the full byte
      Therefore twice as efficient.
      There is a problem in adding

## Slide 13: Example of adding problem
Consider the following
  LDAA #$17
  ADDA #$28
Result is 0011 1111 B which is not BCD
  How do we fix this?
  Add 6 to low digit and high digit
  Or.. Use the DAA instruction

## Slide 14: DAA Instruction
DAA stands for Decimal Adjust Accuumulator
  Only works with A register
  Adds 6 to lower nibble and higher nibble if necessary, otherwise no effect
  Consider the following
  LDAA #$47 ; A = $47
  ADDA #$25 ; A = A + 25 H RESULT IS 6C H
  DAA ; ADUST FOR BCD ADDITION, RESULT IS 72 H

## Slide 15: Summary of DAA action after any instruction
If lower nibble is GT 9, or if H=1, add 0110 to lower nibble
If upper nibble is GT, 9 or if C=1, add 0110 to upper nibble.
Conclusion, H status bit is for BCD arithmetic
CLRA ; A = 0
ADDA #$09 ; A = 9 H
ADDA #$ 08 ; A = 9 H + 8 H = 11, H =1
DAA ; A = $ 17, 6 IS ADDED

## Slide 16: Subtraction of unsigned numbers
Two different instructions
  SUB
  SBC – Subtract with borrow
    Uses Carry Flag for the borrow
  SUBA – A = A – Operand
  Subtraction uses 2’s complement method
  If C = 0 a priori, SUBA Looks like
    Take 2’s complement of source operand
    Add it to A
    Invert the carry

## Slide 17: Neg Instruction
After execution of SUBA, if C = 0 the result is positive
If C = 1, the result is negative
Destination has 2’s complement of result
NEG (negate) may be used to change this
NEG performs 2’s complement

## Slide 18: Example of SUBA
LDAA #$3F ; A = 3F H
SUBA #$23 ; A = A – 23 H
0011 1111
- 0010 0011
Same as 0011 1111
+ 1101 1101 twos complement of $23
_________
1 0010 1100 Inverted C bit is 0 (result is positive)
Programmer must verify status of C bit to determine sign of number.

## Slide 19: Example using NEG
; Program to subtract 6E H from 4C H
MYREG EQU $820 ; LOCATION OF NUMBER TO BE SUBTRACTED
LDAA #$6E ; A = 6E H
STAA MYREG ; STORE 6E H AT LOCATION 820 H
LDDA #$4C ; A = 4C H
SUBA MYREG ; A = DE, INVERTED C = 1
BCC NEXT ; IF C = 0 BRANCH TO NEXT TARGET
NEGA ; TAKE 2’S COMPLEMENT OF A
NEXT STAA MYREG ; RESULT IS STORED IN MYREG
; 6E = 01101110 2’S COMPLIMENT OF THIS IS 1001 0010
; AFTER THE SUBA COMMAND C =1 AND THE RESULT IS NEGATIVE WE DO NOT
; BRANCH AND 2’S COMPLEMENT IS TAKEN AND MYREG = 22 H MAGNITUDE OF
; NEGATIVE RESULT

## Slide 20: SBCA SUBTRACT WITH BORROW
Used for multi-byte numbers
Handles borrow of lower byte
C flag holds borrow
If C = 1 prior to execution, 1 is subtracted from result

## Slide 21: Example with SBCA
; Program to subtract 2 16 bit numbers eg $2762 - $1296 assuming location 806 H
; stores 12 H and location 807 H stores 96 H, store result in same locations with big
; endian convention. We are looking for the result of 14CC
LDAA #$62 ; LOAD LOW BYTE
SUBA $807 ; A = 62 H – 96 H = CC H, C = BORROW = 1
STAA $807 ; STORE LOW BYTE
LDAA #$27 ; LOAD HIGH BYTE
SBCA $806 ; A = 27 – 12 – 1 = 14 H
STAA $806 ; STORE HIGH BYTE
; Since these are 16 bit or 2 byte numbers, we could us the instruction SUBD
LDD #2762 ; LOAD D REGISTER
SUBD $806 ; SUBTRACT THE VALUES AT $806 AND $807
STDD $806 ; STORE RESULT

## Slide 22: Some Widely Used Arithmetic Instructions
Instruction | Action
ADDA | Add operand to register A
ADCA | Add operand to register A with carry
ADDD | Add operand to register D
SUBA | Subtract operand from register A
SBCA | Subtract operand from register A with carry
SUBD | Subtract operand from Reg D
DAA | Decimal Adjust Addition

## Slide 23: Multiplication of unsigned numbers
Byte by Byte and Word by Word are supported by the HCS12
  MUL ; A x B AND 16 BIT RESULT STORED IN D
    ONE OPERAND IS IN A REG, SECOND IN B REG
    LOWER BYTE RESULT IS IN B
    UPPER BYTE RESULT IS IN A

## Slide 24: Multiplication examples
; Multiply 25 H by 65 H
LDAA #$25 ; FIRST OPERAND IN A
LDAB #$65 ; SECOND OPERAND IN B
MUL ; 25 H x 65 H = E99 H IN REG D
; A = 0E H, B = 99 H
;
; 16 bit multiplication
LDD #500 ; D = 500 DECIMAL
LDY #700 ; Y = 700 DECIMAL
EMUL ; 500 x 700 = 350000 = 55730 H
; Y = 0005 H, D = 5730 H

## Slide 25: Unsigned Multiplication and Division Summary
Inst | Multiplication | Operand 1 | Operand 2 | Result | 
MUL | Byte x Byte | A | B | D , A high | B low
EMUL | Word x Word | D | Y | Y:D Y high | D low
Inst | Division | Numerator | Denominator | Quotient | Remainder
IDIV | Word/Word | D | X | X | D
EDIV | Dword/word | Y:D | X | Y | D

## Slide 26: Division Examples
; divide 255 decimal by 10 decimal
LDD #255 ; D = 255 DECIMAL
LDX #10 ; X = 10 DECIMAL
IDIV ; 255/10 = 25 REMAINDER 5
` ; X = 25 DECIMAL AND D = 5
;
; divide 90FF24 H by 1000 decimal
;
LDD #$FF24 ; LOWER WORD
LDY #$90 ; UPPER WORD
; 90FF24 H = 9502500 DECIMAL
LDX #1000 ; X = 1000 DECIMAL
EDIV ; Y:D/X = 9502 (251E H) REMAINDER 500 (1F4)

## Slide 27: Division Application Example ADC
; ADC provides Hex data between 00 and FF H. Conversion to decimal is accomplished
; by dividing by 10 repetitively and saving remainder. This program converts FD H to
; decimal with byte by byte division using locations 822 – 824 H to store results where 824 is LSD
RMNDL EQU $824 ; LOCATION OF LEAST SIGNIFICANT DIGIT
RMNDM EQU $823 ; LOCATION OF MIDDLE SIGNIFICANT DIGIT
RMNDH EQU $822 ; LOCATION OF HIGH SIGNIFICANT DIGIT
MYNUM EQU $FD ; FD H = 253 D
MYDEN EQU 10 ; DENOMINATOR IS 10 DECIMAL
ORG $8000 ; START AT 8000 H
LDD #MYNUM ; LOAD NUMERATOR IN REGISTER D
LDX #MYDEN ; LOAD DENOMINATOR IN REGISTER X
IDIV ; 253/10 = 25 R 3
STAB RMNDL ; SAVE REMAINDER ALWAYS LT 10, 3 IN THIS CASE
XGDX ; EXCHANGE D AND X FOR NEW NUMERATOR 25
LDX #MYDEN ; X = 10
IDIV ; 25/10 = 2 R 5
STAB RMNDM ; SAVE NEXT DIGIT, 5 IN THIS CASE
XGDX ; X IS NOW 5 AND D IS 2
STAB RMNDH ; STORE FINAL DIGIT 2