## Slide 1: Section 5.2
Logic Instructions and Programs

## Slide 2: Some Widely Used Boolean Logic Instructions in HCS12
Instruction | Action
ANDA | AND A with memory location
ORAA | OR A with memory location
EORA | EXCLUSIVE OR A with memory location
COMA | 1’s Compliment (Invert) A, result is NOT A

## Slide 3: AND
Format
  ANDA (operand)
  Truth Table
X | X | X AND Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 4: AND Example
; Example of 35 H anded with 0F H
LDAA #$35
ANDA #$0F
; Result
; $35 0011 0101
; AND $0F 0000 1111
; 0000 0101
; $05 WITH Z = 0, N = 0

## Slide 5: OR
X | Y | X OR Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
FORMAT
  ORAA (operand)
  Truth Table

## Slide 6: Example of OR
; 04 H ored with 30 H
LDAA #$04 ; A = 04 H
ORAA #$30 ; A = 04 H OR 30 H
; RESULT
; $04 0000 0100
; OR $30 0011 0000
; 0011 0100
; $34 with Z = 0, N = 0

## Slide 7: Exclusive Or
Format
  EORA Operand
  Register A and Operand are exclusively ored and the result is stored in A
  Operand my be a RAM Address or an immediate value
  The instruction will affect Z and N flags
    N is B7 of the result
    Z = 1 for a zero result
X | Y | X XOR Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 8: XOR Example
; 54 H and 78 H are exclusively ored
LDAA #$54
EORA #$78
; Result
; $54 0101 0100
; EORA $78 0111 1000
; 0010 1100
; $2C WITH Z = 0, N = 0

## Slide 9: XOR Example XOR with known value
; XOR a value with itself
LDAA PORTB ; LOADS BYTE FROM PORTB
EORA PORTB ; XOR WITH A
BNE OVER ; BRANCH IF PORTB HAS CHANGED
; $45 0100 0101
; XOR $45 0100 0101
; 0000 0000
; $00 WITH Z = 1

## Slide 10: Using XOR to toggle bits of operand
LDAA #$FF
EORA PORTB ; ALL BITS ARE CHANGED
STAA PORTB ; TO OPPOSITE VALUE
; $FF 1111 1111
; XOR $45 0100 0101 ; ASSUMED VALUE
; 1011 1010
; $BA
; COULD WE DO THIS WITH COM INSTRUCTION?

## Slide 11: COM the compliment instruction
Performs 1’s complement on target register
X | NOT X
0 | 1
1 | 0
LDAA #$FF ; A IS ALL 1’S
STAA DDRB ; PORTB IS OUTPUT
LDAA #$55 ; A = 55 H OR 0101 0101 B
OVER COMA ; A = 1010 1010 B OR AA H, WE’VE SEEN THIS BEFORE
STAA PORTB ; CONTINUOUSLY TOGGLE PORTB
BRA OVER ; LOOP TO OVER

## Slide 12: Negate command NEG
Takes two’s compliment of A or RAM location
See below example
; Find 2’s compliment of 85 H
LDAA #$85 ; A = 85 H
NEGA ; PERFORM 2’S COMPLIMENT ON A
; RESULT
; 85 H 1000 0101
; NEGA 0111 1010 1’S COMPLIMENT
; + 1 0111 1011 2’S COMPLIMENT = 7B H

## Slide 13: BCLR Instruction
Used to clear specific bits of I/O port or any RAM location
This command ANDs inverted mask byte with contents of location and places result back into location
LDAA #$FF ; A IS ALL 1’s
STAA PORT B ; PORTB IS 1111 1111
BCLR PORT B, %11000000 ; CLEAR BITS 6 AND 7 OF PORT B
; 1100 0000 MASK BYTE
; 0011 1111 MASK BYTE INVERTED
; 1111 1111 PORTB VALUE
; 0011 1111 RESULT BITS 6 AND 7 ONLY ARE CLEARED

## Slide 14: BCLR Example
; Assume that RAM location 806 contains value 9F, we desire to clear bits 0, 2, and 4 only.
DATA1 EQU $806 ; VARIABLE ASSIGNED TO ADDRESS
BCLR DATA1, $00010101 ; BITS 0, 2, AND 4 TO BE CLEARED
; INVERTED MASK 11101010
; AND 9F H 10011111
; RESULT 8A 10001010

## Slide 15: BSET Instruction
Used to make specific bits high
Mask byte has specific bits
BSET Instruction ORs mask byte with value in location and stores result in location
LDAA #$00 ; A = 00 H
STAA PORTB ; PORTB = 0000 0000
BSET PORTB, %00000011 ; Set bits 0 and 1 of PORTB
; MASK BYTE 0000 0011
; OR 0000 0000
; RESULT 0000 0011

## Slide 16: BSET Example
; Given that RAM location 806 H contains value 8A, our objective is to set bits 4, 5, 6, and 7 high with out
; affecting the other bits at the location.
DATA EQU $806 ; VARIABLE ASSIGNED TO LOCATION
BSET DATA2, %11110000 ; SET BITS 4, 5, 6, AND 7 ONLY
;
; MASK BYTE 1111 0000
; OR 8A H 1000 1010
; RESULT FA 1111 1010

## Slide 17: Another BSET EXAMPLE
; Given that PB2 is used to control an outdoor light, and further that PB controls an indoor light, we desire a
; code segment to turn on the outdoor then turn off the indoor light.
BSET DDRB, %00100100 ; PB5 AND PB2 ARE OUTPUT
BSET PORTB, %00000100 ; PB2 (OUTDOOR) IS 1
BCLR PORTB, %00100000 ; PB5 (INDOOR) IS 0

## Slide 18: BRSET Instruction
Branch if certain bits set high
Mask Byte indicates bits to check
BRSET performs AND on mask byte and inverted memory location
  The branches if all bits are 0

## Slide 19: BRSET Instruction Example
; Given that PB7 is used to monitor the status of a switch, write a program to toggle PA0 when ever the switch
; goes high. Then further analyze the cases of PB7 = 1 and PB7 = 0
BCLR DDRB, %10000000 ; PB7 IS INPUT
BSET DDRA, %00000001 ; PA0 IS OUTPUT
BACK BRSET PORTB, %10000000 , TOG ; BRANCH TO TOG IF PB7 IS HIGH
BRA BACK ; KEEP CHECKING IT
TOG BCLR PORTA, %00000001 ; PA0 = 0
BSET PORTA, %00000001 ;PA0 = 1
BRA BACK ; CHECK PB7 AGAIN
; CASE 1 PB7 = 1 MASK BYTE 1000 0000
; AND INVERTED PORTB 0000 0000
; RESULT 0000 0000 IT WILL BRANCH
; CASE 2 PB7 = 0 MASK BYTE 1000 0000
; AND INVERTED PORTB 1000 0000
; RESULT 1000 0000 IT WILL NOT BRANCH

## Slide 20: BRCLR Instruction
Branch if clear branches if certain bits of target are low. .
Mask byte indicates the bits to be checked
The instruction performs a logical and between the mask byte and the target location and branches if all bits are low.

## Slide 21: BRCLR Example
; You are given that PB2 is used to monitor the status of a switch. Write a program to toggle PA7 whenever
; PB is low. Further analyze each of the two possible cases.
BCLR DDRB, %00000100 ; PB2 IS INPUT
BSET DDRA, %10000000 ; PA7 IS OUTPUT
BACK BRCLR PORTB, %00000100, TOG ; BRANCH TO TOG IF PB2 = 0
BRA BACK ; KEEP LOOKING AT PB2
TOG BCLR PORTA, %10000000 ; PA7 = 0
BSET PORTA, %10000000 ; PA7 = 1
BRA BACK ; KEEP LOOKING AT PB2
; CASE 1 PB2 = 1 MASK BYTE 00000100
; AND PB2 00000100
; RESULT 00000100 WILL NOT BRANCH
; CASE 2 PB2 = 0 MASK BYTE 00000100
; AND PB2 00000000
; RESULT 00000000 WILL BRANCH