## Slide 1: Section 5.3
Compare Instruction and Programs

## Slide 2: Compare instructions
In the case of unsigned data these instructions compare a value with the contents of a register
  Value can be immediate or in a RAM location
  The Z and C flags are set based on the results of the comparison
  It is really a subtraction
  Except the values of the operands do not change
  I say again, the values of the operands do not change
  Note the following table

## Slide 3: HCS12 Compare Instructions
Command | Result | C = 0 | C = 1 | Z = 1
CBA | Compare A with B | A > B | A < B | A = B
CMPA | Compare A with value | A > VALUE | A < VALUE | A = VALUE
CMPB | Compare B with value | B > VALUE | B < VALUE | B = VALUE
CPD | Compare D with 16 bit value | D > VALUE | D < VALUE | D = VALUE

## Slide 4: Example Using CMPA
; Program determines if data on PORTB contains the value 99 H, If so, write ‘Y’ to Port A else write ‘N’ to Porta.
BCLR DDRB, %11111111 ; PORT B IS INPUT
BSET DDRA, %11111111 ; PORT A IS OUTPUT
LDAA #’N’ ; A IS ASCII N
STAA PORTA ; PORT A IS ‘N’
LDAA #$99 ; A IS 99H
BACK COMPA PORTB ; IS PORTB = 99 H?
BNE BACK ; NO KEEP CHECKING
LDAA #’Y’ ; YES WRITE TO PORT A
STAA PORTA ; PORT A IS ‘Y’

## Slide 5: Another Example Using CMPA
; PROGRAM FINDS THE GREATER OF TWO VALUES AND PLACES THE LARGER ONE IN LOCATION $820
VAL1 EQU 54 ; 54 D
VAL2 EQU 27 ; 27 D
BIG EQU $820 ; VARIABLE ASSIGNED TO LOCATION
LDAA #VAL1 ; A = 54 D
CMPA #VAL2 ; COMPARE 54 D TO 27 D
BCS OVER ; JUMP IF VAL1 < VAL2 (C = 1)
STAA BIG ; VAL1 > VAL2, STORE A INTO BIG

## Slide 6: Using BHI and BLO Instructions for Unsigned Numbers
BCS (branch if carry set) and BCC (branch if carry clear) can be used to transfer control after a compare instruction
Use of BHI (branch if higher) and BLO (branch if lower) is recommended instead
  Many assemblers will assemble the program that way which can be confusing to the programmer
  These instructions are inherently more intuitive

## Slide 7: Example Using BLO Instruction
; Given that PORTB is an input connected to a pressure sensor, the program reads the sensor value looking for a
; value of 75. Three cases are possible
; If P = 75 then A = 75
; If P > 75 then HIGH = P
; If P < 75 then LOW = P
HIGH EQU $820 ; ASSIGN VARIABLES TO LOCATION
LOW EQU $821
BCLR DDRB, %11111111 ; PORTB IS INPUT
LDAA #75 ; BASIS FOR COMPARISON
CMPA PORTB ; COMPARE PORTB WITH 75
BEQ EXIT ; BRANCH IF EQUAL TO 75 (Z = 1)
LDAA PORTB ; GET NEW READING IF NOT EQUAL
BLO LOWER ; BRANCH TO STORE LOW
STAA HIGH ; STORE HIGH
BRA EXIT ; YOU CAN MOVE ALONG NOW
LOWER STAA LOW ; STORE LOW
EXIT ……. ; CONTROL IS TRANSFERRED

## Slide 8: Example Program to Find the Highest Number in a Set
; Given a set of 5 numbers, find the highest and store it in a variable at $810 location.
ORG $840
SET DC.B 69, 87, 96, 45, 75 ; DEFINE CONSTANT BYTE
COUNT EQU $800 ; LOCATION OF COUNT VARIABLE
HIGH EQU $810 ; LOCATION OF HIGHEST NUMBER
LDAA #5 ; A = 5 D
STAA COUNT ; COUNTER VARIABLE INITIALYZED
LDX #SET ; X POINTS TO SET DATA
CLRA ; HIGHEST NUMBER SO FAR IS 0
AGAIN CMPA 0,X ; COMPARE NEXT NUMBER TO HIGHEST
BHI ; BRANCH TO NEXT IF A IS STILL HIGHEST
LDAA 0,X ; A HOLDS NEW HIGHEST
NEXT INX ; POINT TO NEXT NUMBER
DEC COUNT ; DECREMENT COUNT VARIABLE
BNE AGAIN ; DO IT AGAIN IF COUNTER NE 0
STAA HIGH ; HIGH = HIGHEST NUMBER

## Slide 9: Lower Case to Upper Case Conversion
We can use the CMPA instruction to determine if an ASCII character is upper case
Letter | Hex | Binary | Letter | Hex | Binary
A | 41 | 0100 0001 | a | 61 | 0110 0001
B | 42 | 0100 0010 | b | 62 | 0110 0010
C | 43 | 0100 0011 | c | 63 | 0110 011
… | … | … | … | … | …
Y | 59 | 0101 1001 | y | 79 | 0111 1001
Z | 5A | 0101 1010 | z | 7A | 0111 1010
Note the only difference is in Bit 6

## Slide 10: Example of Lowercase to Uppercase Conversion
; The program converts lowercase ASCII to uppercase ASCII. It only operates on data within the ASCII alphabet range.
ORG $850
DATA1 DC.B ‘mY NAME is jOe’ ; define constant byte
ORG $875
DATA2 DS.B 14 ; define space byte 0000 1110 = NUMBER OF CHAR
COUNT EQU $800 ; LOCATION OF COUNT VARIABLE
LDAA #14 ; A = 14 D
STAA COUNT ; INITIALYZE COUNTER AT 14 D
LDX #DATA1 ; X POINTS TO ORIGINAL DATA
LDY #DATA2 ; Y POINTS TO UPPERCASE DATA
BACK LDAA 0, X ; GETS NEXT CHARACTER
CMPA #$61 ; CHECK IF LESS THAN ‘a’
BLO OVER ; IF LOWER, THEN NO CONVERSION
CMPA #$7A ; CHECK IF GREATER THAN ‘z’
BHI OVER ; IF HIGHER THEN NO CONVERSION
ANDA 11011111 ; MASK BIT 5 WHICH IS THE CONVERSION
OVER STAA 0,Y ;STORE UPPER CASE LETTER
INX ; POINT TO NEXT LETTER IN ORIGINAL DATA
INY ; POINT TO NEXT LETTER IN UPPERCASE DATA
DEC COUNT ; DECREMENT COUNTER
BNE BACK ; DON’T WORRY ABOUT THE MULE GOING BLIND, JUST KEEP LOADING THE WAGON

## Slide 11: Summary of Comparison of Unsigned Number Instructions
Instruction | Action | Relation
BHI branch if higher | Branch if C + Z = 0 | A > Value
BHS branch if higher or same | Branch if C = 0 | A >= Value
BLO branch if lower | Branch if C = 1 | A < Value
BHI branch if lower or same | Branch if C + Z = 0 | A <= Value