## Slide 1: Section 5.4
Rotate, Shift Instructions and Data Serialization

## Slide 2: Some Widely Used Rotate and Shift Instructions
Instruction | Action
LSL | Logical shift left memory
LSLA | Logical shift left A
LSR | Logical shift right memory
LSRA | Logical shift right A
ROL | Rotate left memory
ROLA | Rotate left A
ROR | Rotate right memory
RORA | Rotate right A

## Slide 3: Rotating right through carry
RORA
  Bits are rotated from left to right
  Carry Flag becomes MSB
  LSB becomes Carry Flag
  In this case the Carry Flag acts a part of the register
CLC ; C = 0
LDAA #$26 ; A = 26 H = 0010 0110 B, C = 0
RORA ; A = 0001 0011 B, C = 0
RORA ; A = 0000 1001 B, C = 1
RORA ; A = 1000 0100 B, C = 1
RORA ; A = 1100 0010 B, C = 0

## Slide 4: ROR Rotate right memory
Works pretty much the same
MYREG EQU $820 ; LOCATION OF VARIABLE
SEC ; C = 1
LDAA #$75 ; A = 75 H
STAA MYREG ; VALUE OF MYREG IS 75 H = 0111 0101 B, C = 1
ROR MYREG ; MYREG = 1011 1010 B, C = 1
ROR MYREG ; MYREG = 1101 1101 B, C = 0
ROR MYREG ; MYREG = 0110 1110 B, C = 1
ROR MYREG ; MYREG = 1011 0111 B, C = 0

## Slide 5: ROLA Rotate Left Through Carry
Bits are shifted Right to Left
Carry Flag enters at LSB
MSB exits to Carry Flag
Carry Flag operates as part of the register
SEC ; C = 1
LDAA #$15 ; A = 0001 0101 B, C = 1
ROLA ; A = 0010 1011 B, C = 0
ROLA ; A = 0101 0110 B, C = 0
ROLA ; A = 1010 1100 B, C = 0
ROLA ; A = 0101 1000 B, C = 1

## Slide 6: ROL Rotate Left Memory
We can also operate on a memory location
MYRED EQU $820 ; LOCATION OF VARIABLE
CLC ; C = 0
LDAA #$89 ; A = 1000 1001 B
STAA MYREG ; MYREG = 1000 1001 B
ROL MYREG ; MYREG = 0001 0010 B, C =1
ROL MYREG ; MYREG = 0010 0101 B, C = 0
ROL MYREG ; MYREG = 0100 1010 B, C = 0
ROL MYREG ; MYREG = 1001 0100 B, C = 0

## Slide 7: Logical Shift vs Numeric Shift
Logical Shift is for unsigned operands
Arithmetic Shift is for signed operands
Arithmetic Shifts discussed later in the chapter

## Slide 8: Shifting the Bits Right LSRA
Difference from Rotate is that the MSB is loaded with 0 for each shift, not the Carry Bit.
LDAA #$36 ; A = 0011 0110 B
LSRA ; A = 0001 1011 B, C = 1
LSRA ; A = 0000 1101 B, C = 1
LSRA ; A = 0000 0110 B, C = 1
LSRA ; Z = 0000 0011 B, C = 0

## Slide 9: Logical Shift of memory location right LSR
LSR, its not just for register A anymore..
MYREG EQU $820 ; VARIABLE LOCATION
LDAA #$75 ; A = 0111 0101 B
STAA MYREG ; MYREG = 0111 0101 B
SEC ; C = 1
LSR MYREG ; MYREG = 0011 1010 B, C =1
LSR MYREG ; MYREG = 0001 1101 B, C = 0
LSR MYREG ; MYREG = 0000 1110 B, C = 1
LSR MYREG ; MYREG = 0000 0111 B, C = 0

## Slide 10: Logically Shifting Bits Left LSLA
Same concept as LSRA, opposite direction
LDAA #$72 ; A = 0111 0010
LSLA ; A = 1110 0100 B, C = 0
LSLA ; A = 1100 1000 B, C = 1
LSLA ; A = 1001 0000 B, C = 1
LSLA ; A = 0010 0000 B, C = 1

## Slide 11: Logical Shift Left of Memory LSL
Once more with feeling..
MYREG EQU $820
LDAA #$89 ; A = 1000 1001 B
STAA MYREG ; MYREG = 1000 1001 B
LSL MYREG ; MYREG = 0001 0010 B, C = 1
LSL MYREG ; MYREG = 0010 0100 B, C = 0
LSL MYREG ; MYREG = 0100 1000 B, C = 0
LSL MYREG ; MYREG = 1001 0000 B, C = 0

## Slide 12: Serializing Data
This is a way to send a byte of data one bit at a time to a single pin of the microcontroller
Two possibilities
  Use the serial port
    Down side is the limited flexibility available to programmers
  Transfer data one bit at a time and control the sequence of data and spaces between them.
    Serial versions of LCD, ADC, and ROM are becoming popular due to their reduced interconnection density
    We may use rotate instructions to serialize data

## Slide 13: Serializing a Byte of Data
; Program to transfer the value 41 H one bit at a time via PB1. Data transfer is initiated by pulling PB1 High, and
; Terminate it by pulling PB1 High. Send the LSB first
RCOUNT EQU $820 ; ADDRESS OF COUNTER VARIABLE
BSET DDRB, %00000010 ; PB1 IS OUTPUT
CLC ; C = 0
LDAA #8 ; A = 8 D
STAA RCOUNT ; RCOUNT = 8 D
LDAA #$41 ; A = 41 H
BSET PORTB, %00000010 ; START DATA TRANSFER
AGAIN LSRA ; SHIFT RIGHT TO CARRY C = B0 VALUE
BCC OVER ; BRANCH TO OVER IF C = 0
BSET PORTB, %00000010 ; PB1 = 1
BRA NEXT ; BRANCH TO NEXT LABEL
OVER BCLR PORTB, %00000010 ; PB1 = 0
NEXT DEC RCOUNT ; DECREMENT COUNTER
BNE AGAIN ; SHIFT TO GET NEXT BIT
BSET PORTB, %00000010 ;ELSE TERMINATE DATA TRANSFER

## Slide 14: Serially Read a Byte
; Program reads a byte one bit at time and stores the result in a particular RAM location. We read the LSB first
RCOUNT EQU $820 ; LOCATION FOR COUNTER VARIABLE
MYDATA EQU $821 ; LOCATION FOR INCOMING DATA
BCLR DDRB, %10000000 ; PB7 IS INPUT
LDAA #8 ; A = 8 D
STAA RCOUNT ; COUNTER VARIABLE INITIALYZED
CLC ; START WITH CARRY BIT = 0
AGAIN BRCLR PORTB, %10000000 , NEXT ; BRANCH TO NEXT IF PB7 = 0
SEC ; C = 1
RORA ; ROTATE RIGHT WITH CARRY TO A REGISTER A BIT 7
BRA OVER ; BRANCH TO GET NEXT BIT
NEXT CLC ; ELSE C = 0
RORA ; ROTATE RIGHT WITH CARRY TO REGISTER A BIT 7
OVER DEC RCOUNT ; DECREMENT COUNTER
BNE AGAIN ; GET NEXT BIT

## Slide 15: Example code to determine the number of ones in a particular byte
; Program to find the number of ones in a given byte
R1 EQU $820 ; LOCATION OF VARIABLE TO STORE NUMBER OF 1’S
COUNT EQU $821 ; LOCATION OF COUNT VARIABLE
VALUE EQU $822 ; LOCATION OF DATA BYTE
CLC ; C = 0
CLRA ; A = 0
STAA R1 ; INITIAL R1 VALUE IS 0
LDAA #8 ; A = 8 D
STAA COUNT ; INTIALYZE COUNTER TO 8 D
LDAA #$97 ; WE WILL FIND THE NUMBER OF 1’S IN 97 H OR 1001 0111 B
STAA VALUE ; DATA BYTE INITIALYZED
AGAIN ROLA ; ROTATE LEFT THRUOU CARRY
BCC NEXT ; IF C = 0 BRANCH TO NEXT
INC R1 ; ELSE INCREMENT THE NUMBER OF 1’S
NEXT DEC COUNT ; DECREMENT COUNTER
BNE AGAIN ; GET NEXT BIT FOR 8 TIMES

## Slide 16: Example swap operation to reverse high and low nibble of a byte
VARIABLE EQU $820 ; RAM LOCATION OF SCRATCH VARIABLE
LDAA #$72 ; A = 0111 0010 B
STAA VARIABLE ; VARIABLE = 0111 0010 B
LSRA ; A = 0011 1001 B
LSRA ; A = 0001 1100 B
LSRA ; A = 0000 1110 B
LSRA ; A = 0000 0111 B
LSL VARIABLE ; VARIABLE = 1110 0100
LSL VARIABLE ; VARIABLE = 1100 1000
LSL VARIABLE ; VARIABLE = 1001 0000
LSL VARIABLE ; VARIABLE = 0010 0000
ORAA VARIABLE ; A = 0010 0111 = 27 H