## Slide 1: Section 5.5
BCD and ASCII Conversion

## Slide 2: ASCII and BCD Codes for Digits 0-9
Key | ASCII (hex) | Binary | Unpacked BCD
0 | 30 | 0011 0000 | 0000 0000
1 | 31 | 0011 0001 | 0000 0001
2 | 32 | 0011 0010 | 0000 0010
3 | 33 | 0011 0011 | 0000 0011
4 | 34 | 0011 0100 | 0000 0100
5 | 35 | 0011 0101 | 0000 0101
6 | 36 | 0011 0110 | 0000 0110
7 | 37 | 0011 0111 | 0000 0111
8 | 38 | 0011 1000 | 0000 1000
9 | 39 | 0011 1001 | 0000 1001

## Slide 3: Packed BCD to ASCII Conversion
Real Time Clock
  Provides data in packed BCD
  In order to display it must be converted to ASCII
In order to convert packed BCD
  First convert it to unpacked BCD
  Then the unpacked BCD is ORed with 0011 0000 (30 H)
  Let packed BCD = 29 H = $02, $09 unpacked = $32, $39 ASCII
  Binary 0010 1001 = 0000 0010 unpacked = 0011 0010 ASCII
  Second nibble = 0000 1001 unpacked = 0011 1001 ASCII

## Slide 4: Example of converting packed BDC to 2 ASCII Numbers and placing in specific memory locations
; Register A contains the packed BCD. The program converts the packed BCD to 2 ASCII numbers and stores
; them into locations $806 and $807
BCDVAL EQU $29 ; THE PACKED BCD VALUE TO BE CONVERTED
HASCI EQU $806 ; HIGH BYTE OF ASCII
LASCI EQU $807 ; LOW BYTE OF ASCII
LDAA BCDVAL ; A = 29 H
ANDA #$0F ; MASK THE UPPER NIBBLE
ORAA ; MAKE IT ASCII
STAA LASCI ; SAVE IT LASCI = 39 H = ‘9’
LDAA BCDVAL ; A = 29 H
ANDA #$ F0 ; MASK LOWER NIBBLE A = 20 H
LSRA ; SHIFT RIGHT 4 TIMES TO GET UPPER NIBBLE TO LOW NIBBLE
LSRA
LSRA
LSRA
ORAA #$30 ; MAKE IT ASCII
STAA HASC ; SAVE IT HASCI = 32 H = ‘2’

## Slide 5: ASCII to Packed BCD Conversion
First convert ASCII to unpacked BCD (to get rid of the 3) , then combine to make the packed BCD
; convert 4 and 7 to packed BCD
MYBCD EQU $820 ; LOCATION OF PACKED BCD VARIABLE
LDAA #’4’ ; A = 34 H
ANDA #$0F ; MASK UPPER NIBBLE
LSLA ; SHIFT LEFT 4 TIMES FOR LOWER NIBBLE
LSLA
LSLA
LSLA
STAA MYBCD ; MYBCD = 40 H
LDAA #’7’ ; A = 37 H
ANDA #$0F ; MASK UPPER NIBBLE
ORAA MYBCD ; A = $47
STAA MYBCD ; MYBCD = $47 A PACKED BCD