## Slide 1: Chapter 6
Advanced Addressing Modes, Look up Table, Macros and Modules

## Slide 2: Objectives
Upon Completion of this Chapter, students will be able to:
Code HCS12 Assembly language programs using advanced addressing modes
Code HCS12 instructions to manipulate a look up table
Access fixed data residing in the program ROM space
Discuss how to create Macros and Modules
Code HCS12 programs for ASCII and BCD data conversion
Code HCS12 programs to create and test the checksum byte
List the advantages of macros and modules in programming
Understand the concepts of GLOBAL and EXTERNAL in modular programming

## Slide 3: Advanced Indexed Addressing Mode
In the indexed addressing mode, a register is used as a pointer to the data location
  4 registers may be used for this purpose in the HCS12
  Namely X, Y, SP, and PC
  These are 16 bit registers
  In most applications we will not use PC since it used by the CPU
One advantage of the indexed addressing mode is that it makes accessing data dynamic rather than static.
Note the following examples

## Slide 4: One way to skin the cat
; The program copies the value 55 H into RAM memory locations $840 t0 $844 using extended addressing mode
LDAA #$55 ; A = 55 H
STAA $840 ; $840 = 55 H
STAA $841 ; $841 = 55 H
STAA $842 ; $842 = 55 H
STAA $843 ; $843 = 55 H
STAA $844 ; $844 = 55 H

## Slide 5: Another way to skin the cat
; Program to copy the value 55 H into locations $840 thru $844 using indexed addressing mode with out a loop
LDAA #$55 ; A =55 H
LDX #$840 ; LOAD POINTER WITH FIRST ADDRESS
STAA 0,X ; $840 = 55 H
INX ; NOW X POINTS TO $841 HEX
STAA 0,X ; $841 = 55 H
INX ; NOW X POINTS TO $842 HEX
STAA 0,X ; $842 = 55 H
INX ; NOW X POINTS TO $843 HEX
STAA 0,X ; $843 = 55 H
INX ; NOW X POINTS TO $844 HEX
STAA 0,X ; $844 = 55 H

## Slide 6: Yet another way to skin this cat
; Program to copy 55 H into locations 840 H thru 844 H using a loop.
COUNT EQU $810 ; LOCATION OF COUNTER VARIABLE
LDAA #$5 ; A = 5 H
STAA COUNT ; COUNT = 5 H
LDX $840 ; FIRST RAM ADDRESS
LDAA #$55 ; A = 55 H
B1 STAA 0,X ; STORE 55H INTO POINTED TO ADDRESS
INX ; POINT TO NEXT ADDRESS
DEC COUNT ; DECREMENT COUNTER
BNE B1 ; LOOP UNTIL COUNT = 0
; You might verify this using Code Warrior

## Slide 7: Comments about previous example
Using a loop is most efficient in the general case
  This is only possible because of the indexed addressing mode
  Looping is not possible in extended addressing mode
  This is the main difference between extended and indexed modes
Think about the case where we might want to send a string
  This would much more efficient using indexed mode
Note the next example

## Slide 8: Example using extended addressing mode
; You are given that RAM locations $830 thru $834 contain a string of ASCII data, ie. $830 = ‘H’, $831 = ‘E’,
; $832 = ‘L’, $833 = ‘L’, $834 = ‘O’. The object is to get each character and send it to Port B one byte at a time
; using extended addressing mode
BSET DDRB, $11111111 ; PORTB IS OUTPUT
LDAA $830 ; A = ‘H’
STAA PORTB ; PORTB = ‘H’
LDAA $831 ; A = ‘E’
STAA PORTB ; PORTB = ‘E’
LDAA $832 ; A = ‘L’
STAA PORTB ; PORTB = ‘L’
LDAA $833 ; A = ‘L’
STAA PORTB ; PORTB = ‘L’
LDAA $834 ; A = ‘O’
STAA PORTB ; PORTB = ‘O’

## Slide 9: Example using indexed addressing mode
; You are given that RAM locations $830 thru $834 contain a string of ASCII data, ie. $830 = ‘H’, $831 = ‘E’,
; $832 = ‘L’, $833 = ‘L’, $834 = ‘O’. The object is to get each character and send it to Port B one byte at a time
; using indexed addressing mode
COUNT EQU $810 ; LOCATION OF COUNT VARIABLE
LDAA #$5 ; A = 5 H
STAA COUNT ; COUNT = 5 H
LDX $830 ; X POINTS TO FIRST ADDRESS
B2 LDAA 0,X ; LOAD THE POINTED TO VALUE INTO A
STAA PORTB ; NOW PORTB CONTAINS VALUE IN A
INX ; INCREMENT POINTER
DEC COUNT ; DECREMENT COUNTER
BNE B2 ; LOOP UNTIL COUNT = 0

## Slide 10: Auto increment for indexed addressing
We have auto increment and auto decrement options in HCS12 for X, Y and SP registers
This is accomplished using the CLR instruction
Increment decrement values may be -8 thru +8
PC may not be auto incremented/decremented
Note the following table

## Slide 11: Auto Increment/Decrement for CLR Instruction
Instruction | Function
CLR 0,X | X stays the same after clearing pointed to location
CLR 1,X+ (post increment) | X increments after clearing pointed to location
CLR 1,+X (pre increment) | X is incremented then pointed to location is cleared
CLR 1, X- (post decrement) | X decrements after clearing pointed to location
CLR 1,-X (pre decrement) | X is decremented then pointed to location is cleared

## Slide 12: Example to clear 16 ram locations starting at $840
; using auto increment to clear the locations
COUNT EQU $810 ; LOCATION OF COUNT VARIABLE
LDAA #16 ; A = 16 D
STAA COUNT ; COUNT = 16 D
LDX #$840 ; FIRST LOCATION
B1 CLR 1,X+ ; RAM LOCATION CLEARED THEN X INCREMENTED BY 1
DEC COUNT ; DECREMENT COUNTER
BNE B1 ; LOOP UNTIL COUNTER = 0

## Slide 13: Example to sum contents of memory locations
; add the data in locations $840 thru $843, store the result in locations 806 and 807 H, given $840 = 7D H,
; $841 = EB H, $842 = C5 H, and $843 = 5B H
HBYTE EQU $806 ; LOCATION OF HIGH BYTE OF RESULT, BIG ENDIAN
LBYTE EQU $807 ; LOCATION OF LOW BYTE OF RESULT, BIG ENDIAN
COUNT EQU $810 ; LOCATION OF COUNT VARIABLE
LDAA #4 ; A = 4 D
STAA COUNT ; COUNT INITIALYZED TO 4 D
LDX #$840 ; FIRST MEMORY LOCATION
CLRA ; A = 0
STAA HBYTE ; HBYTE = 0
; CONTINUED ON NEXT SLIDE

## Slide 14: Sum Example Continued
; Picking back up with the loop
B1 ADDA 1, X+ ; ADD A AND INCREMENT POINTER
BCC OVER ; BRANCH TIO OVER, IF NO CARRY
INX HBYTE ; ELSE INCRENT THE HIGH BYTE
OVER DEC COUNT ; DECREMENT THE COUNTER VARIABLE
BNE B1 ; LOOP UNTIL COUNT = 0
STAA LOWBYTE ; STORE THE LOWBYTE RESULT

## Slide 15: EXAMPLE PROGRAM TO COPY 5 BYTES OF DATA
; The program copies a block of 5 bytes of data from RAM locations starting at $830 to a RAM block starting at
; $860. Given that $830 = ‘H’, $831 = ‘E’, $832 = ‘L’, $833 = ‘L’, $834 = ‘O’
COUNT EQU $810 ; LOCATION OF COUNT VARIABLE
LDAA #$5 ; A = 5 H
STAA COUNT ; COUNTER INITIALYZED
LDX $830 ; LOWER BLOCK
LDY $860 ; HIGH BLOCK
B2 LDAA 1,X+ ; GET POINTED TO BYTE
STAA 1,Y+ ; STORE IN POINTED TO BYTE
DEC COUNT ; DECREMENT COUNTER
BNE B2 ; LOOP UNTIL COUNTER = 0
; Now that $860 = ‘H’, $861 = ‘E’, $862 = ‘L’, $863 = ‘L’, $864 = ‘O’

## Slide 16: Example Program to Copy 20 Bytes
; Program copies a block of 20 bytes starting at RAM location $830 to a block of 20 bytes starting at $860
COUNT EQU $810 ; LOCATION OF COUNT VARIABLE
LDAA #10 ; A = 10 D
STAA COUNT ; COUNTER INITIALYZED
LDX #$830 ; START OF SOURCE
LDY #$860 ; START OF TARGET
B3 LDD 2, X+ ; GET THE WORD AT SOURCE AND INCREMENT POINTER BY 2
STD 2, Y+ ; COPY TO TARGET AND INCREMENT POINTER BY 2
DEC COUNT ; DECREMENT COUNTER
BNE B3 ; LOOP 10 TIMES UNTIL COUNTER = 0

## Slide 17: Effective Address in Indexed Addressing Mode
In this mode we have 5-, 9-, or 16- bit signed offset as displacement
The displacement is added to the indexed register to calculate the effective address
For example in LDAA 5,X , X + 5 is the effective address. In this case A is loaded with the 5th byte from the beginning address pointed to by X
We can also use the accumulators A, B, and D to hold the offset value
Note the following example

## Slide 18: Effective Address Example
; Given X = $1200, find the effective address for the following cases
; LDAA 10,X
; LDAA 14,X
; LDAA -3,X
; LDAA 10,X Effective: $1200 + 10 = $120A
; LDAA 14,X Effective: $1200 + 14 = $120E
; LDAA -3,X Effective: $1200 – 3 = $11FD