## Slide 1: Section 6.2
Accessing Look Up Table in Flash

## Slide 2: Overview
We have mainly focused on RAM access thus far
In the single chip mode of HCS12..
  We normally do not use any RAM space for storing code
  We use Flash memory to store static data
  EEPROM is also used for storing critical date (Chapter 14)
We will cover the access fixed data residing in Flash
But first how do we get it there in the first place?

## Slide 3: DC.B and fixed data in flash
This directive is widely used to allocate ROM in byte sized chunks
  In other words 8 bit fixed data
  Widely used to define ASCII strings
    Remember ‘ for character
    “ for strings
  Code warrior allows use of FCB instead of DC.B to define values up to $FF
  DC.W may be used to define values up to $FFFF
How do we access the fixed data?

## Slide 4: Example of Storing Data into ROM
; Data into ROM
ORG $8500 ; ROM ADDRESS
DATA1 DC.B 28 ; 28 D (1C H) 8500 = 1C H,
DATA2 DC.B %00110101 ; BINARY (35 H) 8501 = 35 H
DATA3 DC.B $39 ; HEX 8502 = 39 H
ORG $8510 ; ROM ADDRESS
DATA4 DC.B ‘Y’ ; ASCII CHARACTER 8510 = 59 H
DATA5 DC.B ‘2’,’0’,’0’,’5’ ; ASCII NUMBERS 8511 = 32 H, 8512 = 30 H, 8513 = 30 H, 8514 = 35 H
ORG $8518 ; ROM ADDRESS
DATA6 DC.B “HELLO RONNY” ; ASCII STRING 8518 = 48 H, 8519 = 45 H, 8520 & 8521 = 4C ….
END

## Slide 5: Example program writing from ROM to PORTB Using a counter
; given $8500 = ‘U’, $8501 = ‘S’, and $8502 = ‘A’, program sends this data to PORTB one byte at a time
COUNT EQU $810 ; LOCATION OF COUNT VARIABLE
ORG $8000 ; BEGINNING OF PROGRAM ROM
BSET DDRB,%11111111 ; PORTB IS OUTPUT
LDAA #$3 ; A = 3 H
STAA COUNT ; COUNTER INITIALYZED
LDX #MYDATA ; X = $8500
B1 LDAA 0,X ; LOAD POINTED TO VALUE INTO A
STAA PORTB ; WRITE A TO PORTB
INX ; GET NEXT POINTED TO VALUE
DEC COUNT ; DECREMENT COUNTER
BNE B1 ; LOOP 3 TIMES
ORG $8500 ; LOCATION OF ASCII data
MYDATA DC.B “USA” ; ASCII STRING AT $8500

## Slide 6: Example Program to Read from ROM and Write to PORTB Using Null
; assume the same ROM setup is the same as previous example
ORG $8000 ; STARTING ADDRESS OF PROGRAM ROM
BSET DDRB, $11111111 ; PORTB IS OUTPUT
LDX #MYDATA ; X POINTS TO $8500
B2 LDAA 0,X ; LOAD POINTED TO VALUE
BEQ OVER ; EXIT IF 0 IS LAST VALUE
STAA PORTB ; WRITE POINTED TO VALUE TO PORTB
INX ; INCREMENT POINTER
BRA B2 ; GET NEXT VALUE
OVER BRA OVER ; USE THIS OR GO BACK TO MONITOR PROGRAM
ORG $8500 ; DATA AREA
MYDATA DC.B “USA”,0 ; NOTE NULL CHARACTER AFTER STRING

## Slide 7: Example using null and auto-increment
; assume same data at $8500
ORG $8000 ; BEGINNING OF PROGRAM IN ROM
BSET DDRB,%11111111 ; PORTB IS OUTPUT
LDX #MYDATA ; LOADS POINTER TO $8500
B3 LDAA 1,X+ ; COPY AND INCREMENT POINTER
BEQ OVER ; EXIT IF ENCOUNTER NULL
STAA PORTB ; ELSE WRITE A TO PORTB
BRA B3 ; GET NEXT CHARACTER
OVER BRA OVER ; THIS OR MONITOR PROGRAM
ORG $8500 ; START OF DATA
MYDATA DC.B “USA”,0 ; NOTE NULL CHARACTER

## Slide 8: Example of selecting data from ROM dataset
; assume that ROM space starting with $8500 contains personal information such as first name, last name,
; phone number, etc. Program reads last name and sends it to PORTB.
COUNT EQU $810 ; ADDRESS OF COUNT VARIABLE
ORG $8000 ; START OF PROGRAM
BSET DDRB,%11111111 ; PORTB IS OUTPUT
LDAA #$4 ; A = 4 H
STAA COUNT ; COUNT IS INITIALYZED
LDX #MYDATA ; POINTS AT $8500
B2 LDAA 12,X ; COPY THE LOCATION AT X + 12 TO A
STAA PORTB ; WRITE TO PORTB
INX ; INCREMENT POINTER SEE NEXT SLIDE

## Slide 9: Personal Data Continued
; we left off at INX
DEC COUNT ; DECREMENT COUNT VARIABLE
BNE B2 ; LOOP 4 TIMES UNTIL COUNT = 0
BRA $ ; STAY HERE
;---------------------------------------------------------------------------- DATASET
ORG $8500 ; START OF DATA
MYDATA FCB “John “ ; FIXED WIDTH 12 CHARACTERS
FCB “Dewey “ ; FIXED WIDTH 12 CHARACTERS
FCB “111-999-9998” ; FIXED WIDTH 12 CHARACTERS
END

## Slide 10: Example to copy ROM data to RAM 1 byte at a time
; Data is stored in ROM starting at $8500 with the string “The Promise of World Peace” store in RAM starting
; at $840 one byte at a time
ORG $8000 ; START OF PROGRAM
LDX #MYDATA ; LOAD POINT AT START OF DATA
LDY $840 ; POINTS AT START OF RAM TARGET
B5 LDAA 1, X+ ; GET DATA FROM SOURCE
BEQ EXIT ; EXIT IF THIS IS LAST BYTE (NULL)
STAA 1, Y+ ; STORE IN TARGET
BRA B5 ; GO BACK TO B5
EXIT BRA EXIT ; KEEP LOOPING
ORG $8500
MYDATA DC.B “The Promise of World Peace”,0

## Slide 11: A Couple More Points
The Code Warrior Simulator will allow us to verify the contents in RAM and ROM for a particular program
Look up Table and reading from Flash
  Look up table is a widely used concept
  Allows access of frequently used elements with minimum operations
  For example,
    LDAA A,X retrieves data at effective address of X+A
    See next example
Writing to Flash ROM involves manipulation of CCR see Chapter 14

## Slide 12: Example to get value from PORTA, square it and write it to PORTB
; Assume values to be squared are between 0 and 9 stored in PB3 – PB0, it is desirable to use a look up table to increase speed of execution
ORG $8000 ; START OF PROGRAM
BCLR DDRB,%00001111 ; PB3 – PBO OF PORT B ARE INPUT
BSET DDRA,%11111111 ; PORTA IS OUTPUT
LDX #XSQR_TABLE ; X POINTS AT $8500
B2 LDAA PORTB ; READ VALUE FROM PORTB
ANDA #$0F ; MASK UPPER BITS
LDAA A,X ; GET SQUARE FROM LOOKUP TABLE
STAA PORTA ; WRITE TO PORTA
BRA B2 ; KEEP LOOKING AT PORTB
ORG $8500 ; START OF LOOK UP TABLE
XSQR_TABLE DC.B 0,1,4,9,16,25,36,49,64,81

## Slide 13: Example to read status of switches and send ASCII representation to PORTA
; Values are determined by values from PB2 (SW2) – PB0 (SW0)
ORG %8000 ; START OF PROGRAM
BCLR DDRB,%00000111 ; PB2 – PB0 C0NFIGURED AS INPUT
BSET DDRA,%11111111 ; PORTA IS OUTPUT
LDX #ASCIITABLE ; POINTS AT $8500
B6 LDAA PORTB ; GET VALUE FROM PORTB
ANDA #$7 ; MASK UPPER 5 BITS
LDAA A,X ; GET ASCII FROM LOOK UP
STAA PORTA ; WRITE IT TO PORTA
BRA B6 ; KEEP LOOKING AT PORTB
ORG $8500
ASCIITABLE DC.B ‘0’,’1’,’2’,’3’,’4’,’5’,’6’,’7’