## Slide 1: Section 6.3
Checksum and ASCII Subroutines

## Slide 2: Check Sum Byte in ROM
This is a calculation to assure integrity of ROM
  Transient conditions may cause corruption
  Checksum byte is tagged to the end of a series of data
  It is calculated by adding the bytes of the series together, ignoring carries, then take 2’s compliment of total sum
  This becomes the checksum byte which becomes the last byte of the series
  The result of adding all the bytes including the checksum must be zero
  This analogous to adding a number to its negative
  If one of the numbers in the series has changed the result will not be 0
  Let us look at an example

## Slide 3: Checksum example
Given 4 bytes of hex data:
  25 H, 62 H, 3F H, 52 H
  Adding we get the total sum byte of 18 H where the carry is dropped
  0001 1000 take 1’s 1110 0111 + 1 = 1110 1000 = E8 H 2’s
  Add all to insure integrity results in:
    18H + E8 = 200 H dropping carry => 00 data is not corrupted
If second byte were 22H, corruption
  25 H + 22 H + 3F H + 52 H + E8 H = 1C0 H
  Dropping carry, result C0, data is corrupted

## Slide 4: Checksum Program
; First subroutine retrieves data from code ROM but first the bookkeeping.
MYRAM EQU $860 ; RAM SPACE TO PUT BYTES
COUNT EQU $820 ; RAM LOCATION FOR COUNTER’
COUNT4 EQU 4 ; COUNTER VALUE FOR ADDING 4 BYTES
COUNT5 EQU 5 ; COUNTER VALUE FOR ADDING 5 BYTES INCLUDING CHECKSUM
; MAIN
LDS #$900 ; SET UP STACK
JSR COPYDATA ; THE FIRST SUBROUTINE
JSR CHECKSUM ; THE SECOND SUBROUTINE
JSR TEST ; THIRD SUBROUTINE
BRA $ ; HANG OUT HERE

## Slide 5: Check Sum Program First Subroutine
; Copy data
LDX #MYBYTE ; LOAD POINTER X = $8500 ROM
LDY #MYRAM ; LOAD POINTER Y = $860 RAM LDAA #COUNT4 ; VALUE OF 4
STAA COUNT ; INITIALYZE COUNT
B5 LDAA 1,X+ ; GET VALUE FROM POINTER AND INCREMENT POINTER]
STAA 1,Y+ ; SAVE IN RAM AND INCREMENT POINTER
DEC COUNT ; DECREMENT COUNTER
BNE B5 ; LOOP UNTIL 0
RTS ; RETURN

## Slide 6: Check Sum Second Subroutine to Calculate Check Sum
; Calculating the check sum byte
CALCHECKSUM
LDAA #COUNT4 ; ADDING 4 BYTES
STAA COUNT ; VALUE OF COUNT = 4
LDX #MYRAM ; X POINTS TO TARGET
CLRA ; A = 0
B2 ADDA 1,X+ ; ADD AND INCREMENT POINTER
DEC COUNT ; DECREMENT COUNTER
BNE B2 ; LOOP UNTIL 0
NEGA ; 2’S COMPLEMENT
STAA 0,X ; SAVE CHECKSUM AS LAST BYTE
RTS ; RETURN TO CALLING PROGRAM

## Slide 7: Testing Check Sum Byte, Place on PORTB
; Testing the checksum byte
TESTCHKSUM
BSET DDRB %11111111 ; CONFIGURE PORTB AS OUTPUT
LDAA COUNT5 ; INCLUDE CHECKSUM BYTE
STAA COUNT ; COUNT = 5 D
LDX MYRAM ; X POINTS TO $860 LOCATION
CLRA ; A = 0
B3 ADDA 1,X+ ; ADD AND INCREMENT POINTER
DEC COUNT ; DECREMENT COUNTER
BNE B3 ; LOOP UNTIL 0
CMPA #0 ; IS A = 0?
BEQ G1 ; IF RESULT 0 THEN GOOD
; CONTINUED ON NEXT SLIDE

## Slide 8: Testing Check Sum Continued
LDAA #’B’ ; ELSE RESULT IS BAD
STAA PORTB ; SEND RESULT TO PORTB
RTS ; RETURN TO CALLING PROGRAM
G1 LDAA #’G’ ; RESULT IS GOOD
STAA PORTB ; SEND RESULT TO PORTB
RTS ; RETURN TO CALLING PROGRAM
; BOOKKEEPING
ORG $8500
MYBYTE FCB $25, $62, $3F, $52, $00
END

## Slide 9: BCD to ASCII Conversion
Many Real Time Clocks Provide Data in BCD
  To display it we must convert it to ASCII
  The following example converts packed BCD to ASCII and sends it to PORTB for display
  Note Chapter 12 for advice on displaying to L

## Slide 10: BCD to ASCII Conversion
Many Real Time Clocks Provide Data in BCD
  To display it we must convert it to ASCII
  The following example converts packed BCD to ASCII and sends it to PORTB for display
  Note Chapter 12 for advice on displaying to LCD
  Note Chapter 16 for advanced use of this program
  Refer to Chapter 5 for BCD to ASCII conversion

## Slide 11: Packed BCD to ASCII conversion program
; Initialization
MYRAM EQU $860 ; RAM TO PUT BYTES
ASCRAM EQU $870
COUNT EQU $820 ; RAM LOC FOR COUNTER
CNT4 EQU 4 ; BCD BYTES
CNT8 EQU 8 ; ASCII BYTES
; MAIN
LDS #$900 ; SET UP STACK
JSR COPYDATA ; FIRST SUBROUTINE
JSR CONVERSION ; SECOND SUBROUTIND
JSR DISPLAYDATA ; DISPLAY RESULTS
BRA $ ; HANG OUT HERE

## Slide 12: Copying Data Packed BCD to ASCII
; Copy data from ROM to RAM
COPYDATA
LDX #MYBYTE ; LOAD POINTER X TO $8500
LDY #MYRAM ; POINT TO TARGET
LDAA #CNT4 ; A = 4 D
STAA COUNT ; INTITIALYZE COUNTER
B5 LDAA 1,X+ ; GET BYTE OF BCD FROM ROM, INCREMENT POINTER
STAA 1,Y+ ; SAVE TO RAM, INCREMENT POINTER
DEC COUNT ; DECREMENT COUNTER
BNE B5 ; LOOP TIL COUNT = 0
RTS ; RETURN TO CALLING PROGRAM

## Slide 13: Convert Packed BCD to ASCII
; Convert packed BCD to ASCII
BCDTOASCII
LDX #MYRAM ; X = $860
LDY #ASCRAM ; Y = $870
LDAA #CNT4 ; A = 4
STAA COUNT ; COUNT INITIALYZED
B6 LDAA 0,X ; BET BCD VALUE
ANDA #$F0 ; MASK LOWER NIBBLE
LSRA ; SHIFT RIGHT 4 TIMES TO GET UPPER NIBBLE
LSRA
LSRA
LSRA
; CONTINUED ON NEXT SLIDE

## Slide 14: Convert Packed BCD to ASCII continued
ORAA #$30 ; MAKE IT ASCII
STAA 1,Y+ ; STORE AND INCREMENT COUNTER
LDAA 1,X+ ; GET BCD DATA AND INCREMENT POINTER
ANDA #$0F ; MASK UPPER NIBBLE
ORAA #$30 ; MAKE IT ASCII
STAA 1,Y+ ; STORE IT
DEC COUNT ; DECREMENT COUNTER
BNE B6 ; LOOP UNTIL COUNT = 0
RTS ; RETURN TO CALLING PROGRAM

## Slide 15: Send ASCII Data to PORTB
; Send ASCII to PORTB
DISPLAY
BSET DDRB, $11111111 ; PORTB IS OUTPUT
LDAA CNT8 ; A = 8 D
STAA COUNT ; COUNTER INITIALYZED
LDX #ASCRAM ; LOAD POINTER
B3 LDAA 1,X+ ; COPY RAM TO A AND INCREMENT POINTER
STAA PORTB ; COPY A TO PORTB
DEC COUNT ; DECREMENT COUNTER
BNE B3 ; LOOP UNTIL COUNTER = 0
RTS ; RETURN TO CALLING PROGRAM

## Slide 16: Packed BCD to ASCII wrap up
; some bookkeeping details
ORG $8500 ; START OF ROM
MYBYTE FCB $25, $67, $39, $52
END

## Slide 17: Binary (hex) to ASCII
Many ADC chips provide output in binary (hex)
  We need to convert it to ASCII to display
  One subroutine gets the binary data and converts it to decimal
  Then the decimal data is converted to ASCII
  According to Big Endian Convention where the low digit is high address

## Slide 18: Binary to ASCII Conversion Program
; Initialization
RMNDL EQU $832 ; LEAST SIGNIFICANT DIGIT
RMNDM EQU $831 ; MIDDLE SIGNIFICANT DIGIT
RMNDH EQU $830 ; MOST SIGNIFICANT DIGIT
MYDEN EQU 10 ; DIVIDE BY 10
COUNT EQU $810 ; LOCATION OF COUNTER
CVAL EQU 3 ; COUNTER VALUE
UNPBCD EQU $830 ; LOCATION OF BINARY (HEX)
RESULT EQU $840 ; LOCATION OF ASCII RESULT

## Slide 19: Binary (hex) to ASCII main
; main
LDS #$900 ; INITIALYZE STACK POINTER
BCLR DDRB, %11111111 ; PORTB IS INPUT
LDAB PORTB ; GET VALUE AT PORTB
JSR BINDECCON ; BINARY TO DECIMAL CONVERSION
JSR DECASCIICON ; DECIMAL TO ASCII CONVERSION
BRA $ ; HANG OUT

## Slide 20: Binary (hex) to Decimal Conversion
; Binary (hex) to decimal conversion
BINDECCON
LDX #MYDEN ; X = 10 D
IDIV ; D/X = 253/10 = 25 R3
STAB RMNDL ; STORE REMAINDER HIGH ADDRESS
XGDX ; EXCHANGE D AND X TO GET NEW NUMERATOR
LDX #MYDENT ; X = 10 D
IDIV ; D/X
STAB RMNDM ; STORE REMAINDER MIDDLE ADDRESS
XGDX ; GET HIGH REMAINDER
STAB RMNDH ; STORE HI REMAINDER
RTS ; RETURN TO CALLING PROGRAM

## Slide 21: Binary (hex) to ASCII, converting decimal to ASCII
; Convert decimal to ASCII
DECASCIICON
LDAA #CVAL ; A = 3
STAA COUNT ; COUNTER INITIALYZED
LDX #UNPBCD ; POINTS TO $830
LDY #RESULT ; POINTS TO $840
B3 LDAA 1,X+ ; GET DEC DIGIT AND INCREMENT POINTER
ADAA #$30 ; MAKE IT ASCII
STAA 1,Y+ ; STORE RESULT AND INCREMENT POINTER
DEC COUNT ; DECREMENT COUNTER
BNE B3 ; LOOP UNTIL COUNTER = 0
RTS ; RETURN TO CALLING PROGRAM
END