## Slide 1: Section 5.6
Signed Number Concepts and Arithmetic Operation

## Slide 2: Concept of signed numbers in computers
Both negative and positive numbers are encountered in daily experience.
Therefore computers must be able to accommodate this.
The MSB is set aside for the sign in signed numbers
  0 represents positive
  1 represents negative
8 bit operands
  Bit 7 contains the sign
  N flag in the CCR is a copy of Bit 7
  Highest positive number is 127
  Negative Number Magnitude is represented by 2’s Complement
  This conversion is accomplished by the assembler

## Slide 3: Representation of -5 D
; How the HCS12 would represent -5 D
; 0000 0101 5 in 8 bit binary unsigned
; 1111 1010 1’s compliment
; 0000 0001 add 1 for 2’s compliment
; 1111 1011 result is FB H

## Slide 4: Representation of -34 D
; -34 D in representation in Hex
; 0011 0100 34 H unsigned
; 1100 1011 1’s complement
; 0000 0001 Add 1
; 1100 1100 Result is CC H, N = 1

## Slide 5: Represent -128 D
; Representation of -128 D
; 1000 0000 128 in unsigned binary
; 0111 1111 1’s compliment
; 0000 0001 Add 1 for 2’s compliment
;1000 0000 Result is 80 H and N = 1
; Note that 128 D unsigned = signed -128 D

## Slide 6: Byte sized signed number ranges, recall the -128 to +127 range of conditional branches
Decimal | Binary | Hex
-128 | 1000 0000 | 80
-127 | 1000 0001 | 81
-126 | 1000 0010 | 82
… | … | …
-2 | 1111 1110 | FE
-1 | 1111 1111 | FF
0 | 0000 0000 | 00
+1 | 0000 0001 | 01
+2 | 0000 0010 | 02
… | … | …
+127 | 0111 111 | 7F

## Slide 7: The overflow problem in signed number operations
This is noted by raising the V flag in the CCR
; example of overflow
LDAA #96 ; A = 0110 0000
ADDA #70 ; A = 96 D + 76 D = 1010 0110
; A = A6 H, = -90 D, INVALID
; B7 = 1, RESULT IS NEGATIVE
; REGISTER COULD CONTAIN MAX OF + 127 D
; HOWEVER, V = 1, INDICATING OVERFLOW

## Slide 8: When is the overflow flag set?
Either of the following conditions cause V = 1
  There is a carry from Bit 6 to Bit 7 but no carry from Bit 7
  There is a carry from Bit 7 but no carry from Bit 6 to Bit 7
Note in either case we do not have a carry from both

## Slide 9: Example of V and N flags
; note the role of the V and N flags
LDAA #-128 ; A = -128 D = 1000 0000 B = 80 H
ADDA #-2 ; A = -128 D – 2 D = 1000 000 + 1111 1110 = 0111 1110
; N = 0, A = $7E =+126 D, INVALID
; SOLUTION
; -128 1000 0000
; + -2 1111 1110
; = -130 1111 1001 WITH N = 0 AND V = 1
; V= 1 INDICATES RESULT OF +126 D IS WRONG

## Slide 10: Another V and N Flag example
; Note the V and N flags in the following
LDAA #-2 ; A = 1111 1110 = $FE
ADDA #-5 ; A = -2 D + -5 D = -7 D = F9 H
; V = 0
; -2 1111 1110
; + -5 1111 1011
; = -7 1111 1001 CARRY FROM BIT 6 AND BIT 7 => V = 0 AND N = 1
; RESULT IS CORRECT

## Slide 11: Yet another V and N flag example
; note the V and N flags in the following
LDAA #+7 ; A = 0000 0111
ADDA #+18 ; A = +7 D + +18 D = 0000 0111 + 0001 0010 = 0001 1001
; A = =7 D + +18D = +25 D, N = 0 POSITIVE, V = 0 NO CARRIES B7 OR B6
; +7 0000 0111
; + +18 0001 0010
; = +25 0001 1001 V = 0, N =0 CORRECT POSITIVE RESULT

## Slide 12: Summary signed number addition
V determines validity of result
  V = 1 result is invalid
  V = 0 result is valid
  N = 0 result is positive
  N = 1 result is negative
For unsigned arithmetic monitor the C flag
For signed arithmetic monitor the V flag
There are branch instructions for use with signed numbers

## Slide 13: Branch instructions for Signed numbers
Instruction | Action
BMI Branch if minus | Branch if N = 1
BPL Branch if plus | Branch if N = 0
BVS Branch if V set | Branch if V = 1
BVC Branch if V clear | Branch if V = 0

## Slide 14: 16 Bit Signed Numbers
Decimal | Binary | Hex
-32,768 | 1000 0000 0000 0000 | 8000
-32,767 | 1000 0000 0000 0001 | 8001
-32,766 | 1000 0000 0000 0010 | 8002
… | … | …
-2 | 1111 1111 1111 1110 | FFFE
-1 | 1111 1111 1111 1111 | FFFF
0 | 0000 0000 0000 0000 | 0000
+1 | 0000 0000 0000 0001 | 0001
+2 | 0000 0000 0000 0010 | 0002
… | … | …
+32,766 | 0111 1111 1111 1110 | 7FFE
+32,767 | 0111 1111 1111 1111 | 7FFF

## Slide 15: More about 16 bit signed numbers
Bit 15 is set aside for sign
The overflow flag is set in either of 2 cases
  Carry from Bit 14 to Bit 15, but no carry from Bit 15
  Carry from Bit 15, (C = 1) but no carry from Bit 15 to Bit 15
As in 8 bit signed numbers it is one or the other but not both

## Slide 16: Let us look at an example
; note the status of the V, N, and C flags of CCR in the following
LDD #$6E2F ; D = 28,207 D
ADDD #$13D4 ; D = 28,207 D + 5076 D = 33,283 D
; 6E2F 0110 1110 0010 1111
; + 13D4 0001 0011 1101 0100
; = 8203 1000 0010 0000 0011 = -32,253 INVALID!, V = 1, C = 1, N = 1

## Slide 17: Another 16 bit signed example
; Note the status of V, N, and C flags of CCR in the following
LDD #$542F ; D = 21,551 D
ADDD #$12E0 ; D = 21,551 D + 4,832 D = 26,383 D
; 542F 0101 0100 0010 1111
; + 12E0 0001 0010 1110 0000
; = 670F 0110 0111 0000 1111 = 26,383 D, VALID, V=0, C =0, N = 0

## Slide 18: Arithmetic Shift
Logical Shift is for Unsigned Numbers
Arithmetic Shift is for Signed Numbers
  Basically the same as logical shift except sign bit copied to the shifted bits
  Two basic instructions
    ASR – Arithmetic shift right
    ASL – Arithmetic shift left
  Consider ASRA
    As the are shifted right in C, the empty bits are filled with the sign bit (MSB)
    May be used to divide a signed number by 2
LDAA #-10 ; A = -10 D = F6 H = 1111 0110 B
ASRA ; ARITMETIC SHIFT RIGHT, A = 1111 1011 = FB H = -5 D

## Slide 19: ASLA vs LSLA
These two instructions do exactly the same thing
  There is really no need for ASL as far as signed numbers are concerned

## Slide 20: Signed Number Comparison
CMPA Instruction is the same for both signed numbers and unsigned numbers
  The branch instruction is different depending
  In unsigned numbers, C bit and Z bit of CCR are checked for >, =, <
  In signed numbers, V, Z, and N are checked
  A > value: V XOR N + Z = 0
  A = value: Z = 1
  A < value: V XOR N = 1

## Slide 21: Branch instructions for Signed Numbers
Instruction | Action
BGE Branch Greater or Equal | Branch if V XOR N = 0
BGT Branch if Greater Than | Branch if V XOR N + Z = 0
BLE Branch if Less Than or Equal | Branch if V XOR N + Z = 1
BLT Branch if Less Than | Branch if V XOR N = 1

## Slide 22: Example of Signed Number Comparison
; Given a 7 day list of temperatures with readings containing positive and negative numbers. We want to find
; the lowest reading and store it in a specific memory location
ORG $850
SIGNTMP DC.B +13,-10, +19, +14, -18, +12, -19 ; DEFINE CONSTANT BYTE TEMPERATURES
COUNT EQU $800 ; LOCATION OF COUNTER VARIABLE
LOW EQU $810 ; LOCATION OF LOW TEMPERATURE
LDAA #7 ; A = 7 D
STAA COUNT ; COUNTER INITIALYZED TO 7 D
LDX #SIGNTMP ; X POINTS TO TEMP DATA
LDAA #$7F ; SET A TO HIGHEST POSSIBLE
AGAIN CMPA 0, X ; COMPARE NEXT TEMP TO LOWEST
BLE NEXT ; BRANCH TO NEXT IF THIS TEMP IS LOWEST
LDAA 0, X ; GET NEXT TEMP
NEXT INX ; POINT TO NEXT TEMP
DEC COUNT ; DEREMENT COUNTER
BNE AGAIN ; KEEP LOOKING FOR LOW TEMP
STAA LOW ; STORE LOW TEMP

## Slide 23: Multiplication of Signed Numbers
Instruction | Multiplication | Operand 1 | Operand 2 | Result
EMULS | Word x Word | D | Y | Y:D Y is High Word, D is Low Word

## Slide 24: Signed Number Division
Instrution | Division | Numerator | Denominator | Quoutient | Remainder
IDIVS | Word/Word | D | X | X | D
EDIVS | Double Word/ Word | Y:D | X | Y | D
Note that if denomitor = 0, C = 1 indicating an error